## Slide 1
Extension of HEVC NAL Unit Syntax Structure
Munsi Haque
April 22, 2012

## Slide 2: On NAL Unit Extension
Motivation
  High level syntax hooks in the “base” HEVC design for its potential extensions
  Efficient NAL unit header design in a unified fashion with an extension segment
Highlights in Extension Segment
  A Generic type of extension to include HEVC NAL Unit extension syntax elements
  A single1-bit-flag to differentiate the extension part from “base”
  Syntax parameters are register-type with fixed-sizes (2 to 3 bytes long)
  Address various extension combinations of scalability and multi-view coding

## Slide 3: HEVC NAL Unit & Extension
nal_unit( NumBytesInNALunit ) { | Descriptor
forbidden_zero_bit | f(1)
nal_ref_flag | u(1)
nal_unit_type | u(6)
NumBytesInRBSP = 0 | 
nal_byte_1 | u(8)
if ((nal_byte_1 & 8) > 0) { // Extension part | 
nal_flag_set | u(8)
if ((nal_byte_1 & 16) ==0) { | 
nal_bytes_2 | u(16)
NumBytesInRBSP +=3 | 
} | 
else { | 
nal_bytes_3 | u(24)
NumBytesInRBSP +=4 | 
} | 
} | 
NumBytesInRBSP += 1 | 
for( i = nalUnitHeaderBytes; i < NumBytesInNALunit; i++ ) { | 
if( i + 2 < NumBytesInNALunit && next_bits( 24 ) = = 0x000003 ) { | 
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
i += 2 | 
emulation_prevention_three_byte /* equal to 0x03 */ | f(8)
} else | 
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
} | 
} | 
Proposed NAL Unit with Extension
HEVC NAL Unit (CD)
nal_unit( NumBytesInNALunit ) { | Descriptor
forbidden_zero_bit | f(1)
nal_ref_flag | u(1)
nal_unit_type | u(6)
NumBytesInRBSP = 0 | 
temporal_id | u(3)
reserved_one_5bits | u(5)
for( i = nalUnitHeaderBytes; i < NumBytesInNALunit; i++ ) { | 
if( i + 2 < NumBytesInNALunit && next_bits( 24 ) = = 0x000003 ) { | 
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
i += 2 | 
emulation_prevention_three_byte /* equal to 0x03 */ | f(8)
} else | 
rbsp_byte[ NumBytesInRBSP++ ] | b(8)
} | 
} | 

## Slide 4: nal_byte_1 Syntax Element
reserved (4-bits) | ext_flag1 (1-bit) | temporal_id (3-bits)
nal_id_mask2 (3-bits) | ext_flag2 (1-bit) | ext_flag1 (1-bit) | nal_id_mask1 (3-bits)
2 Configurations for HEVC NAL Unit - Base and Extensions
HEVC Base : ext_flag1 = 0
2) HEVC Extensions: ext_flag1 = 1;
a) ext_flag2 = 0 (nal_bytes_2), 1 (nal_bytes_3)
nal_id_mask1 | nal_IDs | Example Sizes | HEVC Base & Extensions
001 | temporal_id | u(3) | All cases
010 | priority_id | u(6) | Scalable & Multi-view
100 | dependency_id | u(3) | Scalable & Multi-view
Default Examples – (nal_id_mask2, nal_id_mask1)
Scalable => (001, 111)
Multi-view => (010, 011)
Multi-view Scalable => (010, 111)
and so on….
nal_id_mask2 | nal_IDs | Example Sizes | HEVC Base & Extensions
001 | quality_id | u(4) | Scalable
010 | view_id | u(6) to u(10) | Multi-view
100 | reserved |  | 
b) Example Bits arrangement in nal_id_mask1 and nal_id_mask2,
indicate which nal_ID is present in next syntax elements

## Slide 5: Extension Syntax Elements (1)
nal_flags_set Syntax Element
nal_flags_set (example) | value
idr_flag | 0000 0001
no_inter_layer_pred_flag | 0000 0010
use_ref_base_pic_flag | 0000 0100
discardable_flag | 0000 1000
output_flag | 0001 0000
anchor_pic_flag | 0010 0000
inter_view_flag | 0100 0000
reserved | 1000 0000
nal_byte_2 Syntax Element
One example of bit allocations for HEVC Extensions
Example-1 (Scalable Video) with IDs - combo : (nal_id_mask2, nal_id_mask1) = (001, 111)
quality_id (4-bits) | dependency_id (3-bits) | priority_id (6-bits) | temporal_id (3-bits)
1 byte

## Slide 6: Extension Syntax Elements (2)
depth_id (4-bits) | texture_id (4-bits) | view_id (7-bits) | priority_id (6-bits) | temporal_id (3-bits)
c) Example-3 (3DV Extension) with different bit-assignment for nal_id_mask2 and nal_IDs
i) Keep nal_id_mask1 the same as before, but change nal_id_mask2 as follows:
ii) IDs - combo: (nal_id_mask2, nal_id_mask1) = (111, 011)
nal_id_mask2 | nal_IDs | Example Sizes | HEVC Base & Extensions
001 | view_id | u(7) | Multi-view
010 | texture_id | u(4) | 3DV Extension
100 | depth_id | u(4) | 3DV Extension
reserved (5-bits) | view_id (10-bits) | priority_id (6-bits) | temporal_id (3-bits)
nal_bytes_3 Syntax Element
Three examples for HEVC Extensions:
Example-1 (Multi-view Video) with IDs - combo: (nal_id_mask2, nal_id_mask1) = (010, 011)
b) Example-2 (Multi-view & Scalable Video) with IDs - combo: (nal_id_mask2, nal_id_mask1) = (010, 111)
reserved (2-bits) | view_id (10-bits) | dependency_id (3-bits) | priority_id (6-bits) | temporal_id (3-bits)