## Slide 1: JCTVC-I0264 AHG5: Harmonized diagonal scans for coefficient coding
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
HM6.0 diagonal scans
  Coefficient Group (CG) scan
  Coefficient scan
Problems
  Need 2x2, 4x4 and 8x8 to generate all patterns
  Extra 8x8 table for 32x32 CG scans
  Only 4x4 is shared
Same sizes but different patterns

## Slide 4: Proposal
Change 32x32 CG scan
  Need 2x2 and 4x4 to generate all patterns
  Scanning tables can be shared for 4x4 and 8x8
Pros
  Remove 4 branches in decoder.
  Save one 8x8 table.
Same sizes and same patterns

## Slide 5: Proposal & results
Compared to HM6.0
Thanks to Qualcomm for cross-checking
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.1% | 0.0% | 0.1% | -0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | -0.1%
Class C | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 0.1%
Class D | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | -0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.3% | 0.1% | 0.0% | -0.1% | -0.2%
Class C | 0.0% | 0.2% | -0.2% | 0.0% | 0.0% | 0.1%
Class D | 0.1% | -0.2% | 0.1% | 0.0% | -0.5% | 0.1%
Class E | 0.2% | -0.9% | 0.8% | 0.1% | -0.2% | 0.0%
Overall | 0.1% | -0.2% | 0.2% | 0.0% | -0.2% | 0.0%
 | 0.1% | -0.2% | 0.2% | 0.0% | -0.1% | -0.1%
Class F | -0.2% | -0.1% | 0.3% | 0.0% | -0.2% | -0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 6: Conclusion
Harmonize diagonal scans
  CG scans can share patterns with coefficient scans
  Generic and neat design
  Less number of tables and branches in HM and clean text in WD
Proposed to adopt into HEVC