## Slide 1: JCTVC-I0265 Chroma QP extension and signalling enhancement
Jun Xu*, Alexis Tourapis**, Ali Tabatabai*, Kazushi Sato*
*:SONY **: Magnum

## Slide 2: Outline
Introduction
Proposal on chroma QP extension
Proposal on chroma QP signaling granularity

## Slide 3: Introduction
In HEVC, Chroma QP is derived from Luma QP the same as AVC:
  Linear in [0,29]
  Nonlinear beyond 29
JCTVC-H0400 proposed to remove the mapping table g_aucChromaScale[52].
  Support higher resolution chroma formats (e.g. 422, 444)
  Concerns raised about coding loss under CTC.
  HEVC reflector discussions about QP prediction and rate control
    luma QP and chroma QP nonlinear relationship in [29, 51] could affect the Rate-Quantization models in rate control.
Chart: QPY
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
ChromaQPoffset = 0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 29 | 30 | 31 | 32 | 32 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | 37 | 38 | 38 | 38 | 39 | 39 | 39 | 39
QPCb = g_aucChromaScale(Clip(0,51, QPY+Cb_QP_offset)),
QPCr = g_aucChromaScale(Clip(0, 51, QPY+Cr_QP_offset)).
Cb/Cr_QP_offset are signalled at PPS

## Slide 4: Proposal on chroma QP extension(1/2)
Two methods are proposed to extend chroma QP to [0, 51]
  Method A (as in JCTVC-H0400)
    remove mapping table between Chroma and Luma QP
    Pros
      No mapping table
      Flexibility
    Cons
      Nonzero offsets needed for CTC
QPCb = Clip(0, 51, QPY+Cb_QP_offset)
QPCr = Clip(0, 51, QPY+Cr_QP_offset)

## Slide 5: Proposal on chroma QP extension(2/2)
Method B
  Change semantics of chroma QP offset
  Pros
    Zero offsets meet CTC
    Flexibility
  Cons
    Mapping table stays
QPCb = Clip(0, 51, g_aucChromaScale(QPY)+Cb_QP_offset)
QPCr = Clip(0, 51, g_aucChromaScale(QPY)+Cr_QP_offset)

## Slide 6: Simulation results - Test 1
Test setting
  Method A with zero offsets
QPCb = Clip(0, 51, QPY+Cb_QP_offset)
QPCr = Clip(0, 51, QPY+Cr_QP_offset)
Comments
  Chroma has larger QP compared to HM6.0. More chroma coefficients are quantized to zero.
  Loss for chroma
  Gain for luma
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -1.0% | 6.1% | 6.1% | -0.8% | 5.8% | 5.9%
Class B | -1.2% | 6.3% | 6.1% | -1.0% | 6.3% | 6.2%
Class C | -1.3% | 5.9% | 6.0% | -1.2% | 5.9% | 6.2%
Class D | -1.2% | 5.6% | 6.0% | -1.1% | 5.6% | 6.1%
Class E | -1.0% | 6.1% | 6.7% | -1.0% | 6.1% | 6.4%
Overall | -1.1% | 6.0% | 6.2% | -1.0% | 6.0% | 6.1%
 | -1.1% | 6.6% | 6.8% | -1.0% | 6.5% | 6.9%
Class F | -1.1% | 3.9% | 4.2% | -0.9% | 4.0% | 4.2%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.5% | 12.1% | 11.8% | -0.5% | 11.8% | 12.0%
Class B | -1.2% | 10.2% | 9.6% | -1.1% | 10.3% | 9.2%
Class C | -1.3% | 8.9% | 8.8% | -1.2% | 8.8% | 8.9%
Class D | -1.0% | 8.5% | 8.9% | -1.0% | 8.1% | 8.6%
Class E |  |  |  |  |  | 
Overall | -1.0% | 9.9% | 9.8% | -0.9% | 9.8% | 9.7%
 | -1.0% | 10.2% | 10.1% | -1.0% | 10.0% | 10.0%
Class F | -1.1% | 6.1% | 6.5% | -1.1% | 6.2% | 6.5%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.8% | 9.6% | 9.1% | -0.9% | 9.7% | 9.1%
Class C | -1.0% | 8.9% | 9.3% | -1.0% | 8.5% | 9.2%
Class D | -0.8% | 9.0% | 9.7% | -0.8% | 8.9% | 9.1%
Class E | -0.5% | 7.6% | 9.0% | -0.4% | 8.5% | 9.5%
Overall | -0.8% | 8.9% | 9.3% | -0.8% | 9.0% | 9.2%
 | -0.8% | 9.4% | 9.9% | -0.8% | 9.4% | 9.8%
Class F | -1.2% | 5.7% | 5.9% | -0.9% | 5.0% | 8.1%

## Slide 7: Simulation results - Test 2
Test setting under CTC
  Method A + a non-normative approach (nonzero chroma QP offsets)
Comments
  Exactly same PSNR as HM6.0 for each picture.
  ~0.01% Overhead due to multiple PPS.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Overall | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.01% | 0.01% | 0.01%
Class E |  |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.01% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Overall | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%

## Slide 8: Non-normative approach
To follow HM6.0 CTC, nonzero offsets are sent in PPS for Method A
  Nonzero chroma QP offsets in multiple PPS
  Use PPSID in slice header to select correct offsets for each picture
Example
  RandomAccess QP=37
  First picture in GOP
    Luma QP = 38 (QP_offset=1 in GOP)
    Chroma QP = 35 (in HM6.0 CTC)
    Chroma_QP_offset = -3 (in Test 2)
QPY | <29 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
Chroma QP offset | 0 | 0 | -1 | -1 | -1 | -1 | -2 | -2 | -2 | -3 | -3 | -4 | -4 | -5 | -5 | -6 | -7 | -7 | -8 | -9 | -9 | -10 | -11 | -12
Notes: GOP size for RA is 8 and for LB is 4.

## Slide 9: Conclusion
Proposed to extend Chroma QP
  Flexibility
    Chroma QP covers [0, 51]
  Functionality
    Potential support for other color formats
  A non-normative approach to guarantee almost the same HM6.0 coding performance.
    No impact on other tools.
Proposed to adopt chroma QP extension into HEVC

## Slide 10: Proposal on signaling enhancement
Propose slice level chroma QP offset
  HM6.0 has chroma QP offsets in PPS
  Propose to have finer granularity similar to luma in chroma QP control
  New syntax in slicer header
    slice_qp_delta_cb
    slice_qp_delta_cr
Method A + slice level chroma QP offsets
Method B + slice level chroma QP offsets
QPCb = Clip(0, 51, QPY+Cb_QP_offset+slice_qp_delta_cb)
QPCr = Clip(0, 51, QPY+Cr_QP_offset+slice_qp_delta_cr)
QPCb = Clip(0, 51, g_aucChromaScale(QPY)+Cb_QP_offset+slice_qp_delta_cb)
QPCr = Clip(0, 51, g_aucChromaScale(QPY)+Cr_QP_offset+slice_qp_delta_cr)

## Slide 11: Simulation results - Test 3
Test setting under CTC
  Method A + a non-normative approach + slice level chroma QP offsets:
QPCb = Clip(0, 51, QPY+Cb_QP_offset+slice_qp_delta_cb)
QPCr = Clip(0, 51, QPY+Cr_QP_offset+slice_qp_delta_cr)
Comments
  Exactly same PSNR as HM6.0 for each picture.
  Some small overhead due to new syntax in slice header and multiple PPS.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 12: Conclusion
Proposed to enhance signalling of chroma QP
  Flexibility
  Functionality
    Finer granularity in chroma quality control
Proposed to adopt into HEVC