## Slide 1
1
Cheung Auyeung
Sony Electronics Inc.
April 28, 2012
A proposal to remove redundancy in the context selection of significant_coeff_flag
Notes: 1

## Slide 2: Reduction of Redundancy in Context Selection of Significant Map
Conceptually, HM6 compute significant_coeff_flag in three stages:
  Compute
    cnt = sig(I) + sig(H) + sig(F) + sig(E)
  If cnt<4,
    cnt += sig(B)
  Compute context increment as
    ( (cnt + 1) >> 1 ).
Found redundancy in HM6. For example:
  If after stage 1, cnt is 3.
  Then after stage 2, cnt has a value of 3 or a value of 4.
  After stage 3, the context increment is 2 independently on the value of sig(B) in stage 2.
    The computation in stage 2 is redundant.
Propose to remove redundancy in WD6 and HM6:
  Compute
    cnt = sig(I) + sig(H) + sig(F) + sig(E)
  If cnt<3,
    cnt += sig(B)
  Compute context increment as
    ( (cnt + 1) >> 1 ).
x
I
H
F
E
B

## Slide 3: Proposed Change to HEVC WD6
Replace the number 4 in the following line in HEVC WD6 JCTVC-1003_dk by the number 3:
  When yC is less than ( 1 << log2TrafoHeight ) − 2 and sigCtx is less than 4, the following applies.
  sigCtx = sigCtx + significant_coeff_flag[ xC ][ yC + 2 ] (9‑26)
Proposed replacement text:
  When yC is less than ( 1 << log2TrafoHeight ) − 2 and sigCtx is less than 3, the following applies.
  sigCtx = sigCtx + significant_coeff_flag[ xC ][ yC + 2 ] (9‑26)

## Slide 4: BDR Results
Formal proof provided.
BDR results:
Cross-checked by TI in JCTVC-I0209.
  Thank you very much.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class B | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class C | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class D | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class E | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Overall | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
 | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class F | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 

## Slide 5: Summary
Provide exact results as HM6.0
Removed redundancy in HM6 and WD6.
Propose to be adopted in WD7 and HM7.