## Slide 1
1
Cheung Auyeung
Sony Electronics Inc
April 28, 2012
A Proposal to reduce data dependency in the context selection of significant_coeff_flag
Notes: 1

## Slide 2: A Method to Reduce Data Dependency
Conceptually, HM6 selects the context of significant_coeff_flag for blocks larger than 8x8 in three stages:
  Compute
    cnt = sig(I) + sig(H) + sig(F) + sig(E)
  If cnt<4,
    cnt += sig(B)
  Compute context increment as
    ( (cnt + 1) >> 1 ).
Since in stage 2, the computation of cnt depends on the prior value of cnt, it makes pipelining and SIMD implementation more difficult.
To make pipelining and SIMD implementation easier, propose to remove data dependency in stage 2 :
  Compute
    cnt = sig(I) + sig(H) + sig(F) + sig(E) + sig(B)
  Compute context increment as
    cnt = min( ((cnt + 1) >> 1 ), 2)
Alternative, it can be implemented without any data dependency and branches as:
  Compute
    cnt = sig(I) + sig(H) + sig(F) + sig(E) + sig(B)
  Compute context increment as
    cnt = ( (cnt + 1 – ((cnt+3)>>3)) >> 1 ).
x
I
H
F
E
B

## Slide 3: BDR Results
Formal proof provided.
BDR results:
Cross-checked by TI in JCTVC-I0503.
  Thank you very much.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class B | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class C | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class D | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class E | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Overall | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
 | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Class F | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000% | 0.000000%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 

## Slide 4: Summary
Provide exact results as HM6.0
Reduced data dependency
Propose to be adopted in WD7 and HM7.

## Slide 5: Propose Changes to HEVC WD6
Text from HEVC WD6 JCTC-H1003_dk:
  When yC is less than ( 1 << log2TrafoHeight ) − 2 and sigCtx is less than 4, the following applies.
    sigCtx = sigCtx + significant_coeff_flag[ xC ][ yC + 2 ] (9‑26)
  The variable sigCtx is modified as follows.
    If cIdx is equal to 0 and (xC>>2) + (yC>>2) are greater than 0, the following applies.
      sigCtx = ( (sigCtx + 1) >> 1 ) + 24 (9‑27)
  Otherwise, the following applies.
    sigCtx = ( (sigCtx + 1) >> 1 ) + ( (cIdx > 0) ? 18 : 21 ) (9‑28)
Proposed replacement text:
  When yC is less than ( 1 << log2TrafoHeight ) − 2, the following applies.
    sigCtx = sigCtx + significant_coeff_flag[ xC ][ yC + 2 ] (9‑26)
  The variable sigCtx is modified as follows.
    If cIdx is equal to 0 and (xC>>2) + (yC>>2) are greater than 0, the following applies.
      sigCtx = min( ((sigCtx + 1 ) >> 1 ), 2) + 24 (9‑27)
  Otherwise, the following applies.
    sigCtx = min( ((sigCtx + 1 ) >> 1 ), 2) + ( (cIdx > 0) ? 18 : 21 ) (9‑28)

## Slide 6: Propose Changes to HEVC WD6
Alternate proposed replacement text:
  When yC is less than ( 1 << log2TrafoHeight ) − 2, the following applies.
    sigCtx = sigCtx + significant_coeff_flag[ xC ][ yC + 2 ] (9‑26)
  The variable sigCtx is modified as follows.
    If cIdx is equal to 0 and (xC>>2) + (yC>>2) are greater than 0, the following applies.
      sigCtx = ( (sigCtx + 1 – ((sigCtx+3) >> 3) ) >> 1 ) + 24 (9‑27)
  Otherwise, the following applies.
    sigCtx = ( (sigCtx + 1 - ((sigCtx+3) >> 3) ) >> 1 ) + ( (cIdx > 0) ? 18 : 21 ) (9‑28)