## Slide 1: I0278: HRD Buffering for Bitstreams Starting with CRA Picture
Sachin Deshpande, Andrew Segall
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
HEVC CD supports bitstreams starting with CRA pictures.
In this case leading pictures may exist.
  leading picture: A coded picture that follows some other particular picture in decoding order and precedes it in output order.
When a random access is performed at a CRA picture, leading pictures may be discarded (e.g. by the server) from the bitstream as they are not specified for output and have no effect on the decoding process of any other pictures that are specified for output.
<number>
Notes: <number>

## Slide 3: Proposal
We propose modification to Buffering Period SEI message and to HRD for bitstreams starting with CRA pictures when leading pictures may be discarded.
The proposed HRD modification
  Can reduce the initial buffering latency when starting playback at CRA picture.
  Will guarantee that HRD will not underflow when leading pictures after CRA picture are discarded.
Without the proposed modification HRD could underflow when leading pictures are discarded
<number>

## Slide 4: Proposal : Buffering Period SEI Message
cra_leadingpict_discard_flag equal to 1 (0) indicates the presence (absence) of the initial_cra_cpb_removal_delay[ SchedSelIdx ] and initial_cra_cpb_removal_delay_offset[ SchedSelIdx ] syntax elements. This flag shall not be 1 when the associated picture is not a CRA picture.
initial_cra_cpb_removal_delay[ SchedSelIdx ],
initial_cra_cpb_removal_delay_offset [ SchedSelIdx ] : values for HRD initialization at CRA picture when access units containing leading pictures associated with CRA picture are discarded.

## Slide 5: Proposal
The document proposed syntax and semantics to modify Buffering Period SEI message for bitstreams starting with CRA pictures when leading pictures are present.
  The proposed modification will guarantee that HRD will not underflow when leading pictures after CRA picture are discarded.
We propose to adopt the proposed approach in HEVC.
<number>