## Slide 1: JCTVC-I0280: Quantization Matrices and Deblocking Filtering
Geert Van der Auwera, Rajan Joshi,
Marta Karczewicz

## Slide 2: Summary
HEVC supports the signalling of quantization matrices or scaling lists in the APS.
These matrices can significantly modify the QP values used by the scaling process for various use cases.
The HEVC deblocking filter determines its filtering strength based on QP values without considering the potentially significant QP changes introduced by the quantization matrices, which can lead to either too weak or too strong deblocking strength.
It is proposed to provide signalling of one “equivalent QP change” per signalled quantization matrix in order to appropriately modify the deblocking strength. The method to determine the equivalent QP change is encoder-side only and can be optimized together with the quantization matrices.

## Slide 3: Q-Matrices and Deblocking
Any Q-matrix can be signalled that significantly modifies the QP per transform size and frequency. The problem is that the HM6 deblocking filter is not aware of this.
Let M[i][j] represent elements from the array corresponding to one of the Q-matrices. The typical value range of M[i][j] is 1 to 255 (8-bit) with the value 16 representing no change to the quantization for frequency index (i,j).
“Equivalent QP change” is as follows:
M[i][j] / 16 | QP Change
1/16 | -24
1/8 | -18
1/4 | -12
1/2 | -6
1 | 0
2 | +6
4 | +12
8 | +18
16 | +24

## Slide 4: Q-Matrices and Deblocking
Proposal:
  Encoder determines an “equivalent QP change” per Q-matrix based on average of M[i][j] array elements (low-frequency quadrant)
  Encoder looks up “equivalent QP change” in table (encoder-side only)
  Equivalent QP changes are signalled together with the Q-matrices in APS
  Deblocking filter will adjust the deblocking parameters (table look-up of β and tC parameters) based on the equivalent QP changes for blocks P and Q
Avg QM[i][j] | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
QPQM | -24 | -18 | -14 | -12 | -10 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -2 | -1 | -1 | 0
Avg QM[i][j] | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
QPQM | 1 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 6 | 6
 | … |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Avg QM[i][j] | 224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
QPQM | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23
Avg QM[i][j] | 240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255
QPQM | 23 | 23 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24

## Slide 5: Q-Matrices and Deblocking
High-level syntax changes for the APS:
scaling_list_deblocking_flag enables the signalling of the equivalent QP changes: scaling_list_deblocking[sizeID][matrixID]
scaling_list_param( ) { | Descriptor
scaling_list_present_flag | u(1)
if( scaling_list_present_flag ) | 
for( sizeID = 0; sizeID < 4; sizeID++ ) | 
for( matrixID = 0; matrixID < (sizeID = = 3) ? 2 : 6; matrixID++ ) { | 
scaling_list_pred_mode_flag | u(1)
if( !scaling_list_pred_mode_flag ) | 
scaling_list_pred_matrix_id_delta | ue(v)
else | 
scaling_list( ScalingList[ sizeID ][ matrixID ], sizeID , matrixID ) | 
} | 
scaling_list_deblocking_flag | u(1)
if ( scaling_list_deblocking_flag ) | 
for( sizeID = 0; sizeID < 4; sizeID++ ) | 
for( matrixID = 0; matrixID < (sizeID = = 3) ? 2 : 6; matrixID++ ) { | 
scaling_list_deblocking[ sizeID ][ matrixID ] | se(v)
} | 
} | 

## Slide 6: Q-Matrices and Deblocking
Deblocking filter in encoder and decoder determines what equivalent QP change, QPQM, to apply to the QPY values of the P and Q blocks using the signalled parameters scaling_list_deblocking[sizeID][matrixID]
QPL value for deblocking a luma edge:
    QPL = ( QPY,P + QPQM,P + QPY,Q + QPQM,Q + 1 ) / 2
For a chroma edge:
    QPC = ( QPCr,P + QPQM,P + QPCr,Q + QPQM,Q + 1 ) / 2
    QPC = ( QPcb,P + QPQM,P + QPCb,Q + QPQM,Q + 1 ) / 2
  with QPCr = QP_UV( QPY ) and QPCb = QP_UV( QPY ). QP_UV() is the function that converts the luma QPY into QPCr and QPCb for chrominance

## Slide 7: Q-Matrices and Deblocking
HM6.0: AI-Main, QP=13 (+24=37)

## Slide 8: Q-Matrices and Deblocking
Proposed: AI-Main, QP=13+24=37 for DBF

## Slide 9: Objective Results
BD-rates of HM6.0 anchor compared with default quantization matrices (ScalingList=1) without proposed deblocking filter modification
Proposed deblocking filter modification for Q-matrices does not affect the subjective or objective quality result of the default quantization matrices
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.4% | -3.5% | -3.9% | 0.1% | -3.1% | -3.4%
Class C | 2.4% | -2.0% | -2.5% | 1.8% | -2.0% | -2.3%
Class D | 2.3% | -4.0% | -4.1% | 1.7% | -4.2% | -4.1%
Class E | 1.4% | -0.4% | -0.7% | 0.9% | -0.1% | -0.8%
Class F | 4.8% | 1.5% | 5.1% | 4.1% | 0.1% | 5.8%
Overall | 2.2% | -1.8% | -1.4% | 1.7% | -2.0% | -1.1%
 | 2.2% | -1.7% | -1.2% | 1.6% | -2.0% | -1.1%
Enc Time[%] | 99% |  |  | 98% |  | 
Dec Time[%] | 95% |  |  | 96% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.3% | -3.3% | -4.0% | 0.0% | -3.1% | -3.6%
Class C | 2.5% | -2.3% | -2.6% | 2.0% | -2.1% | -2.5%
Class D | 2.6% | -4.0% | -4.3% | 2.2% | -3.6% | -3.6%
Class E | 1.5% | -0.2% | -1.0% | 1.0% | 0.3% | 0.3%
Class F | 5.0% | 2.3% | 5.3% | 4.1% | 1.1% | 4.1%
Overall | 2.3% | -1.6% | -1.5% | 1.8% | -1.6% | -1.3%
 | 2.2% | -1.6% | -1.4% | 1.7% | -1.7% | -1.2%
Enc Time[%] | 99% |  |  | 96% |  | 
Dec Time[%] | 95% |  |  | 96% |  | 
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.4% | 0.7% | 1.3% | 0.1% | -0.4% | 0.2%
Class B | 2.3% | -2.7% | -2.7% | 1.7% | -3.4% | -3.5%
Class C | 4.5% | -1.9% | -2.3% | 3.4% | -3.4% | -4.0%
Class D | 5.2% | -3.5% | -2.6% | 4.3% | -4.4% | -3.8%
Class E | 1.1% | -1.6% | -1.7% | 0.5% | -1.9% | -1.8%
Class F | 6.1% | 0.1% | 2.5% | 5.4% | -2.3% | 0.0%
Overall | 3.3% | -1.5% | -1.0% | 2.6% | -2.7% | -2.2%
 | 3.2% | -1.4% | -0.9% | 2.5% | -2.6% | -2.1%
Enc Time[%] | 97% |  |  | 98% |  | 
Dec Time[%] | 97% |  |  | 100% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 3.1% | 4.8% | -0.2% | 1.7% | 3.0%
Class B | 0.7% | -2.1% | -2.5% | 0.4% | -2.3% | -2.8%
Class C | 3.7% | 0.3% | -0.5% | 3.4% | -0.4% | -1.1%
Class D | 3.9% | -2.4% | -2.3% | 3.8% | -2.4% | -2.3%
Class E |  |  |  |  |  | 
Class F | 6.8% | 4.2% | 7.3% | 6.3% | 2.4% | 5.0%
Overall | 2.9% | 0.5% | 1.2% | 2.7% | -0.3% | 0.2%
 | 3.0% | 0.6% | 1.2% | 2.7% | -0.2% | 0.2%
Enc Time[%] | 99% |  |  | 97% |  | 
Dec Time[%] | 97% |  |  | 97% |  | 

## Slide 10: Conclusion
Quantization matrices can substantially change the QP values used by the coding process, while the HEVC deblocking filter does not adjust its filtering strength
It is proposed to signal one equivalent QP change per quantization matrix in the APS, to be used by the deblocking filter to adjust the filtering strength appropriately
Optimally determining the equivalent QP changes is an encoder-only process
Subjective and objective quality of default quantization matrices is unaltered by proposed scheme