## Slide 1: Adaptive Thresholds for Greater-Than-1 and Greater-Than-2 Flags
JCTVC-I0281
Nguyen Nguyen, Tianying Ji,
Dake He and Gaelle Martin-Cocher
Notes: <number>

## Slide 2: Introduction
Objective:
  Improve throughput (context-coded bins per pixel) in the average case
JCTVC-H0554:
  Limit the number of greater-than-1 and greater-than-2 flags to (de)code in each CG to 8 and 1, respectively:
    numGreater1Flags = 8
    numGreater2Flags = 1
  Improves throughput in worst and average case
Notes: <number>

## Slide 3: Proposal
  Use information from neighbouring or previous CGs to adjust these limits
  Method A: use R(ight) and L(ower) neighbouring CGs
    if (numGreater1(R) + numGreater1(L) > 1) then
      numGreater1Flags = 2
      numGreater2Flags = 0
  Method B: use previous CGs
    if (numGreater1 > 3) then
      numGreater1Flags = 2
      numGreater2Flags = 0
Notes: <number>

## Slide 4: Benefit and Cost
Benefit:
  Improve throughput in the average case, especially at low QP and for large format sequences
Cost:
  Method A: 2 comparisons, 1 addition, 126 bits
  Method B: 2 comparisons
Notes: <number>

## Slide 5: Comparison against HM-6.0 (Method B)
Context-coded bins
BD-Rate
AI-Main | RA-Main | LD-Main
-1.8 | -1.9 | -0.1
AI-HE10 | RA-HE10 | LD-HE10
-1.9 | -2.0 | -0.2
AI-Main | RA-Main | LD-Main
0.02 | 0.06 | 0.02
AI-HE10 | RA-HE10 | LD-HE10
0.01 | 0.06 | -0.01
Notes: <number>

## Slide 6: Comparison against HM-6.0, low QP (Method B)
Context-coded bins
BD-Rate
AI-Main | RA-Main | LD-Main
-3.9 | -4.7 | -3.5
AI-HE10 | RA-HE10 | LD-HE10
-6.9 | -6.1 | -5.1
AI-Main | RA-Main | LD-Main
-0.01 | 0.05 | 0.11
AI-HE10 | RA-HE10 | LD-HE10
-0.01 | 0.08 | 0.15
Notes: <number>

## Slide 7: Comparison against HM-6.0 (Method A)
Context-coded bins
BD-Rate
AI-Main | RA-Main | LD-Main
-2.5 | -2.4 | -0.3
AI-HE10 | RA-HE10 | LD-HE10
-2.6 | -2.5 | -0.4
AI-Main | RA-Main | LD-Main
0.01 | 0.09 | 0.03
AI-HE10 | RA-HE10 | LD-HE10
0.02 | 0.10 | 0.01
Notes: <number>

## Slide 8: Comparison against HM-6.0, low QP (Method A)
Context-coded bins
BD-Rate
AI-Main | RA-Main | LD-Main
-4.5 | -5.5 | -4.3
AI-HE10 | RA-HE10 | LD-HE10
-7.6 | -6.8 | -5.9
AI-Main | RA-Main | LD-Main
0.00 | 0.14 | 0.17
AI-HE10 | RA-HE10 | LD-HE10
0.00 | 0.22 | 0.28
Notes: <number>