## Slide 1
<number>
JCTVC-H0287 (Non-CE2): Reduced Coefficient Precision for ALF Complexity Reduction
Faouzi Kossentini
9th JCTVC Meeting in Geneva. CH
27 April - 7 May 2012
Notes: <number>

## Slide 2: Summary
In HM6.0, non-center coefficients have the same bit-depth: For the worst-case scenario (QP < 28), the bit-depth of non-center coefficients is equal to 8. The bit-depths are as follows:
Proposed bit-depths for the ALF coefficients:
<number>

## Slide 3: Simulation results
 | All Intra HE10 |  | 
 | Y | U | V
Class A | 0.0% | 0.3% | 0.1%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.1% | 0.2%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.5% | 0.2%
Class F | 0.0% | 0.1% | 0.1%
Overall | 0.0% | 0.2% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
<number>
 | Random Access HE10 |  | 
 | Y | U | V
Class A | 0.0% | 0.2% | 0.1%
Class B | 0.0% | 0.2% | 0.1%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E |  |  | 
Class F | 0.0% | 0.1% | 0.1%
Overall | 0.0% | 0.1% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B HE10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.2% | 0.2%
Class C | 0.0% | 0.3% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.4% | 0.1%
Class F | 0.0% | -0.2% | 0.8%
Overall | 0.0% | 0.1% | 0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay P HE10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.2% | 0.1%
Class C | 0.0% | 0.1% | 0.1%
Class D | 0.0% | -0.1% | -0.2%
Class E | 0.2% | 1.2% | 0.6%
Class F | 0.0% | 0.8% | 0.3%
Overall | 0.0% | 0.4% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 4: Conclusions
<number>
BD-Rates relative to HM 6.0: 0.0%, 0.2% and 0.1% average Y, U and V BD-Rates (respectively)
Complexity relative to HM 6.0:
  Same average encoding/decoding times
  ~25% reduction in average bit-depth of the coefficients: Lower hardware complexity