## Slide 1
<number>
JCTVC-H0289 (Non-CE2): A cross 7x5 shape for ALF complexity reduction
Faouzi Kossentini
9th JCTVC Meeting in Geneva, CH
27 April - 7 May 2012
Notes: <number>

## Slide 2: Summary
In HM6.0’s cross 9x7 + center 3x3 square shape: 10 multiplies and 9 adds per sample
Proposed cross 7x5 filter shape: 6 multiplies and 5 adds per sample are required
<number>

## Slide 3: Simulation results
 | All Intra HE10 |  | 
 | Y | U | V
Class A | 0.2% | -0.6% | -0.5%
Class B | 0.3% | -0.6% | -0.6%
Class C | 0.3% | -0.6% | -0.9%
Class D | 0.1% | -0.6% | -0.7%
Class E | 0.9% | -1.7% | -1.4%
Class F | 0.1% | -0.6% | -0.7%
Overall | 0.3% | -0.7% | -0.8%
Enc Time[%] | 99% |  | 
Dec Time[%] | 99% |  | 
<number>
 | Random Access HE10 |  | 
 | Y | U | V
Class A | 0.5% | 0.6% | 0.7%
Class B | 0.8% | 0.7% | 0.5%
Class C | 0.3% | 0.2% | 0.1%
Class D | 0.3% | -0.1% | 0.0%
Class E |  |  | 
Class F | 0.0% | 0.1% | 0.1%
Overall | 0.5% | 0.4% | 0.3%
Enc Time[%] | 99% |  | 
Dec Time[%] | 96% |  | 
 | Low delay B HE10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.5% | -0.9% | -1.0%
Class C | 0.2% | -0.4% | -0.6%
Class D | 0.1% | -0.5% | -0.5%
Class E | 0.8% | -1.6% | -1.5%
Class F | 0.0% | -0.8% | -0.2%
Overall | 0.3% | -0.8% | -0.7%
Enc Time[%] | 100% |  | 
Dec Time[%] | 96% |  | 
 | Low delay P HE10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | 1.0% | -1.0% | -1.4%
Class C | 0.3% | -0.3% | -0.5%
Class D | 0.0% | -0.3% | -1.0%
Class E | 1.7% | -1.2% | -1.3%
Class F | 0.1% | 0.8% | -0.3%
Overall | 0.6% | -0.4% | -0.9%
Enc Time[%] | 100% |  | 
Dec Time[%] | 96% |  | 

## Slide 4: Conclusions
<number>
BD-Rate relative to HM 6.0: 0.4%, -0.4% and -0.5% average Y, U and V (respectively)
Complexity relative to HM 6.0:
  ~1% reduction in average encoding time
  ~3% reduction in average decoding time
  Software/hardware complexity substantially reduced: 40% less ALF coefficients
  Less encoder/decoder implementation complexity