## Slide 1
JCTVC-I0295: Non-CE
On positive/negative sign
for Category 1,4 Edge Offset in SAO
Hak-Sop Song, Chanyul Kim, Joeng-Bum Choi, Jae-Hwan Joo,
Kyo-Hyuk Lee, Jae-Hyun Kim
Samsung Electronics Co., KOREA

## Slide 2
pixel index
x-1
x
x+1
pixel level
category 1
pixel index
x-1
x
x+1
pixel level
category 2
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 3
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 4
Positive edge offset
Negative edge offset
Edge offset categorization in HM6.0
Positive sign offset for category 1 and 2
Negative sign offset for category 3 and 4
Loss of sharpness and coding gain for special contents

## Slide 3
Proposed method (1/3)
pixel index
x-1
x
x+1
pixel level
category 1
pixel index
x-1
x
x+1
pixel level
category 2
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 3
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 4
Positive/
Negative
Edge offset
Positive/
Negative
Edge offset
Allow positive/negative sign of edge offset for category 1 and 4
Provide coding gain and recover sharpness

## Slide 4
Min_Th(75)
Max_Th(160)
Visibility threshold
Pixel
value
Sensitive
region
Non-sensitive
region
Proposed method (2/3)
Background-luminance dependent function [3]

## Slide 5
if ((category 1 && offset < 0) || (category 4 && offset > 0))
{
if (Min_Th (75) < avgPix < Max_Th (160) && QP>=37) offset = 0;
}
else if (category 2 && offset < 0) offset = 0;
else if (category 3 && offset > 0) offset = 0;
else offset = offset;
Proposed method (3/3)
Offset restriction method using background-luminance dependent function
avgPix : average level of pixels included in each category
Min_Th : Minimum threshold (=75)
Max_Th : Maximum threshold (=160)
QP : Quantization parameter in Slice (=37)

## Slide 6
Objective quality
Average coding gain : 0.4% LB-main/LB-HE10 for class E.
Johnny sequence coding gain : 1.1% LB-main, 1.0% LB-HE10.
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.4% | 0.1% | 0.0% | -0.2% | 0.1%
Class C | 0.0% | 0.2% | -0.1% | 0.0% | 0.1% | 0.1%
Class D | 0.1% | 0.1% | 0.4% | 0.0% | 0.0% | -0.3%
Class E | -0.4% | -0.2% | 0.5% | -0.4% | -0.2% | 0.1%
Class F | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | -0.2%
Overall | -0.1% | -0.1% | 0.2% | 0.0% | 0.0% | 0.0%
 | -0.1% | -0.1% | 0.1% | 0.0% | 0.0% | -0.1%
Enc Time[%] | 99% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 102% |  | 

## Slide 7
Subjective quality (1/8)
BasketballDrive AI_HE10 QP37 Frame 286
HM6.0
Proposed

## Slide 8
Subjective quality (2/8)
BQMall LB_HE10 QP37 Frame 29
HM6.0
Proposed

## Slide 9
Subjective quality (3/8)
BQMall LB_HE10 QP37 Frame 102
HM6.0
Proposed

## Slide 10
Subjective quality (4/8)
BasketballDrive LB_HE10 QP37 Frame 146
HM6.0
Proposed

## Slide 11
Subjective quality (5/8)
BasketballDrive LB_HE10 QP37 Frame 423
HM6.0
Proposed

## Slide 12
Subjective quality (6/8)
BasketballDrillText LB_HE10 QP37 Frame 351
HM6.0
Proposed

## Slide 13
Subjective quality (7/8)
BQTerace AI_HE10 QP37 Frame 194
HM6.0
Proposed

## Slide 14
Subjective quality (8/8)
ChinaSpeed AI_HE10 QP37 Frame 499
HM6.0
Proposed

## Slide 15
Conclusion
Recommend the proposed method to be adapted
  Average coding gain : 0.4% LB-main/LB-HE10 for class E.
  Johnny coding gain : 1.1% LB-main, 1.0% LB-HE10.
Subjective quality is similar to HM6.0

## Slide 16
Reference
[1] B. Bross, W.-J. Han, J.-R. Ohm, G. J. Sullivan, T. Wiegand, “High efficiency video coding (HEVC) text specification draft 6,” ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H1003, Feb. 2012.
[2] W.-S. Kim, D.-K Kwon, “CE8 subset c: Necessity of Sign Bits for SAO Offsets,’’ ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H0434, Feb. 2012.
[3] C.-H. Chou and Y.-C. Li, “A perceptually tuned subband image coder based on the measure of just noticeable distortion profile”, IEEE Trans. on CSVT, vol.5, no. 6, Dec. 1995.
[4] F. Bossen, “Common test conditions,” ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H1100, Feb. 2012.

## Slide 17
WD Text Changes (adds marked in yellow)
7.2.2.8 Sample adaptive offset VLC syntax

## Slide 18
WD Text Changes (adds marked in yellow)

## Slide 19
WD Text Changes (adds marked in yellow)