## Slide 1: Experimental results for Multi-Parameter Probability Up-date in HM6.0
Alexander Alshin
Elena Alshina
JeongHoon Park
Samsung Electronics Co., Ltd

## Slide 2: Summary of proposed changes
Removed | Added
UChar m_ucState; | UChar m_ucCounter; unsigned short iP0,iP1; (+4 bytes per context)
UChar m_aucNextStateMPS[ 64 ]; | 
UChar m_aucNextStateLPS[ 64 ]; | 
UChar sm_aucLPSTable[64][4]; | unsigned short sm_aucLPSTable [64][64];
Void updateLPS ()
{
iP0  =(iP0>>4); iP1  =(iP1>>7);
}
Void updateMPS ()
{
iP0+=(32768iP0)>>4); iP1+=(32768iP0)>>7);
}
JCTVC-I0299 Experimental results for Multi-Parameter Probability Up-date in HM6.0

## Slide 4
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.8% | -0.1% | 0.0% | -0.8% | 0.2% | 0.1%
Class B | -0.7% | -0.6% | -0.5% | -0.7% | -0.6% | -0.6%
Class C | -0.7% | -0.6% | -0.5% | -0.7% | -0.6% | -0.5%
Class D | -0.7% | -0.4% | -0.4% | -0.7% | -0.4% | -0.3%
Class E | -0.7% | -0.9% | -0.8% | -0.7% | -1.0% | -0.7%
Overall | -0.7% | -0.5% | -0.4% | -0.7% | -0.5% | -0.4%
Class F | -0.5% | -0.3% | -0.3% | -0.5% | -0.6% | -0.3%
Enc Time[%] | 104% |  |  | 104% |  | 
Dec Time[%] | 96% |  |  | 97% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | 0.3% | 0.3% | -0.9% | 0.7% | 0.1%
Class B | -0.7% | -0.3% | -0.1% | -0.7% | -0.3% | -0.2%
Class C | -0.6% | -0.2% | -0.2% | -0.6% | -0.4% | -0.2%
Class D | -0.5% | -0.1% | 0.5% | -0.4% | 0.2% | 0.0%
Overall | -0.7% | -0.1% | 0.1% | -0.6% | 0.0% | -0.1%
Class F | -0.4% | -0.1% | 0.0% | -0.4% | -0.2% | -0.1%
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 98% |  |  | 96% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class B | -0.7% | 0.0% | 0.1% | -0.7% | -0.7% | -0.2%
Class C | -0.5% | 0.0% | -0.3% | -0.5% | -0.2% | -0.1%
Class D | -0.4% | 0.5% | 0.6% | -0.5% | 0.1% | 0.5%
Class E | -0.2% | -0.7% | 0.1% | -0.2% | -0.4% | -2.0%
Overall | -0.5% | 0.0% | 0.1% | -0.5% | -0.3% | -0.3%
Class F | -0.3% | 0.2% | -0.2% | -0.2% | -0.8% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 96% |  |  | 97% |  | 

## Slide 5: Conclusion
Based on presented test results
Avg. gain 0.6% ; Avg. Enc/Dec time 100%
we propose adopt multi-parameter probability up-date model for CABAC to the next version of HM s/w and DIS.