## Slide 1
Implicit TU split process for asymmetric partitions
JCTVC-I0308
Geneva, CH, April 2012

## Slide 2: Background
Implicit transform split for symmetric and asymmetric partitions when NSQT is on
(TU is aligned with PU boundary)

## Slide 3: Background (continue)
Implicit transform split for symmetric and asymmetric partitions when NSQT is off
(TU crosses asymmetric PU boundary)

## Slide 4: Proposed
Further TU split for asymmetric partitions when NSQT is off
(TU doesn’t cross asymmetric PU boundary)

## Slide 5: Test results
Reference: HM6.0 – “QuadtreeTUMaxDepthInter==1”
Tested: HM6.0 + I0308 - “QuadtreeTUMaxDepthInter==1”
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.3% | -0.4% | -0.1% | -0.2% | 0.0%
Class B | -0.2% | -0.4% | -0.4% | -0.2% | -0.4% | -0.3%
Class C | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1%
Class D | -0.3% | -0.3% | -0.1% | -0.3% | -0.1% | 0.0%
Class E |  |  |  |  |  | 
Overall | -0.2% | -0.3% | -0.3% | -0.2% | -0.2% | -0.1%
 | -0.2% | -0.4% | -0.3% | -0.2% | -0.2% | -0.2%
Class F | -0.3% | -0.3% | -0.3% | -0.3% | -0.2% | -0.2%
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 98% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.3% | -1.4% | -1.1% | -0.3% | -1.1% | -0.8%
Class C | -0.4% | -0.8% | -0.7% | -0.4% | -0.5% | -0.2%
Class D | -0.5% | -1.5% | -0.9% | -0.5% | -0.8% | -1.2%
Class E | -0.2% | -0.7% | 0.2% | -0.1% | -0.1% | -0.4%
Overall | -0.4% | -1.1% | -0.7% | -0.4% | -0.7% | -0.7%
 | -0.4% | -1.1% | -0.7% | -0.4% | -0.7% | -0.7%
Class F | -0.4% | -0.8% | -0.4% | -0.5% | 0.8% | -0.2%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 98% |  | 

## Slide 6: Test results (continue)
Reference: HM6.0 + I0308 – “QuadtreeTUMaxDepthInter==1”
Tested: HM6.0 + NSQT - “QuadtreeTUMaxDepthInter==1”
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.3% | -0.3% | -0.2% | -0.4% | -0.6%
Class B | -0.4% | -1.4% | -1.3% | -0.3% | -1.3% | -1.2%
Class C | -0.4% | -0.7% | -0.7% | -0.4% | -0.7% | -0.6%
Class D | -0.3% | -0.2% | -0.3% | -0.3% | -0.3% | -0.5%
Class E |  |  |  |  |  | 
Overall | -0.3% | -0.7% | -0.7% | -0.3% | -0.7% | -0.7%
 | -0.3% | -0.7% | -0.7% | -0.3% | -0.7% | -0.7%
Class F | -0.2% | -0.3% | -0.1% | -0.1% | -0.3% | -0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.9% | -2.8% | -2.9% | -0.8% | -2.7% | -2.8%
Class C | -0.8% | -1.8% | -1.8% | -0.7% | -1.5% | -1.8%
Class D | -0.7% | -0.8% | -0.3% | -0.6% | -0.6% | -0.3%
Class E | -1.6% | -2.1% | -2.8% | -1.3% | -2.9% | -1.7%
Overall | -1.0% | -1.9% | -2.0% | -0.8% | -1.9% | -1.7%
 | -1.0% | -1.9% | -1.9% | -0.8% | -1.9% | -1.8%
Class F | -1.0% | -1.8% | -2.1% | -0.7% | -1.9% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 

## Slide 7: Conclusion
Recommend to adopt the further implicit TU split process for asymmetric process when NSQT is off to HM7

## Slide 8
Thanks Samsung’s help on cross-checking!

## Slide 9
Thank you!
www.hisilicon.com