## Slide 1
Restricting Slice Boundaries to LCU Granularity
(JCTVC-I0313)
Tim Hellman and Wade Wan
Broadcom Corporation

## Slide 2: Slice Granularity Complexity
Text allows slices to a 16x16 granularity
  Produces very complicated slice patterns
  Even worse when upper-row availability is added in
JCTVC-I0254

## Slide 3: Opportunity for Error
Availability
  Diagonal availability above & below (SAO/ALF filters)
  Upper-row availability calculation is complicated
  Affects vector generation, spatial prediction, CABAC, filtering
Filtering
  ALF has to pad all these boundaries!
    3 pages of text to describe this padding
  Deblock can have different offsets for every one
Testing
  Many, many corner cases
  Interoperabilty nightmare
JCTVC-I0313

## Slide 4: Why do we have it?
MTU size matching (1500 bytes)
  Added: March 2011
  Reason: allows closer matching of packet size to MTU size, for single slice/packet
How much does this really gain us?
  64x64 LCU: 5-8% loss of packing efficiency w/o fine-grain (E024)
  This means: 5-8% more packets would be generated
Packet Header Overhead
  RTP = 82 bytes. Round up to 100 bytes: 7% of an MTU
  8% more packets with 7% overhead = 0.56% bit-rate increase
  This is dwarfed by the loss of putting one slice/packet (~5%)!
Is this a good complexity tradeoff?
  Application could just use a smaller LCU size
JCTVC-I0313