## Slide 1: Sign data hiding simplification and enhancement JCTVC-I0326
Joel Sole, Jianle Chien, Wei-Jung Chien, Marta Karczewicz

## Slide 2: Introduction
Sign data hiding method was adopted in the last meeting
Sign of the first coefficient in a coefficient group (CG) not coded
  If the distance between the last and first non-zero coefficient in a CG is larger than a threshold
    lastNZPosInCG – firstNZPosInCG >= 4
  Sign embedded in the parity of the sum of the coefficient levels of the CG
    parity = (absSum & 0x1)
    If parity=0 (even), then the first coefficient is positive
    If parity=1 (odd), then the first coefficient is negative
Proposed two methods

## Slide 3: Proposed Methods
Simplify hiding criterion to
  lastNZPosInCG >= 4
  No need to know the position of the first non-zero coefficient in a CG
Hide sign of the last non-zero coefficient in a CG
  Implemented on the top of method 1
  Improves performance because it allows more options to the encoder to hide the sign
Methods cross-checked by Sony in JCTVC-I0466

## Slide 4: Performance
Results in common conditions (CC) and RDOQ off case
Methods cross-checked by Sony in JCTVC-I0466
Method | AI-Main | RA-Main | LB-Main | AI-HE10 | RA-HE10 | LB-HE10
M1 – CC | -0.08 | -0.05 | -0.03 | 0.02 | 0.05 | 0.07
M1 – RDOQ off | -0.09 | -0.11 | -0.18 | -0.11 | -0.10 | -0.08
M2 – CC | -0.13 | -0.07 | -0.15 | -0.03 | -0.03 | -0.02
M2 – RDOQ off | -0.08 | -0.30 | -0.52 | -0.10 | -0.26 | -0.34

## Slide 5: Conclusion
The proposed methods provide a better performance/complexity trade-off of the Sign Data hiding method

## Slide 6
Thank you!