## Slide 1: Table Removal in Contexts Assignment of Last Significant Position (LAST) Coding (JCTVC-I0331)
Liwei Guo, Marta Karczewicz, Wei-Jung Chien

## Slide 2: Introduction
Last significant position (LAST) coding in HM6
  LAST is encoded as a binary string
  Prefix bins ai: encoded with contexts
  Suffix bins bi: encoded using bypass mode
  Context mapping table (of size 28) is used for prefix bin coding of luma
Proposed method: equation-based context derivation
  Removal of context mapping table
  Unification of context derivations for luma and chroma
  Consecutive and sequential context fetching
  Reportedly 0.0% Y BD-rate change

## Slide 3: Context for LAST coding in HM 6
Luma
Chroma
  Chroma context mapping table can be replaced by an equation but luma may not.
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 2 |  |  |  | 
TU 16x16 | 6 | 7 | 8 | 8 | 9 | 9 | 2 |  | 
TU 32x32 | 10 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 2
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 15 | 16 | 17 |  |  |  |  |  | 
TU 8x8 | 15 | 15 | 16 | 16 | 17 |  |  |  | 
TU 16x16 | 15 | 15 | 15 | 15 | 16 | 16 | 16 |  | 

## Slide 4: Proposed Solution
  Equation based context derivation
  Context index is derived using an equation
ctx_idx = m+ (bin_idx >>n)
      bin_idx: index of prefix bin
      m: offset parameter
      n: shift parameter
  Sequential and consecutive context access
  Unification of context derivation for luma and chroma
    Chroma: m = 15, n = log2TUSizeMinus2
Two different settings of (m, n) were tested for luma

## Slide 5: Setting A
Setting A parameters
  m = 3*k + ((k+1)>>2)
  n= (k+3)>>2
  k = log2TUSizeMinus2
  Context assignment with Setting A (same context number as HM6)
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 3 | 4 | 4 | 5 |  |  |  | 
TU 16x16 | 6 | 6 | 7 | 7 | 8 | 8 | 9 |  | 
TU 32x32 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14

## Slide 6: Setting B
Setting B parameters
  m= (k*(k+3)>>1)
  n = 1
  k = log2TUSizeMinus2
  Context assignment with Setting B (with a context reduction of 2)
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 0 | 1 |  |  |  |  |  | 
TU 8x8 | 2 | 2 | 3 | 3 | 4 |  |  |  | 
TU 16x16 | 5 | 5 | 6 | 6 | 7 | 7 | 8 |  | 
TU 32x32 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13

## Slide 7: WD text change (1)

## Slide 8: WD text change (2)
Setting A

## Slide 9: Simulation results – Setting A (Normal QP)
All Intra Main |  |  | All Intra HE10 |  | 
Y | U | V | Y | U | V
-0.01% | 0.01% | 0.01% | 0.00% | 0.00% | -0.01%
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
0.00% | -0.05% | 0.10% | 0.02% | -0.01% | -0.02%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
0.00% | 0.05% | 0.18% | -0.02% | -0.16% | 0.04%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.03% | -0.04% | -0.09% | 0.01% | 0.25% | -0.28%
Common test condition with normal QP (22-37) and low QP (12-27)
Results averaged over all sequences including Class F.
Cross-checked by Samsung.

## Slide 10: Simulation results – Setting A (low QP)
All Intra Main |  |  | All Intra HE10 |  | 
Y | U | V | Y | U | V
-0.01% | 0.01% | -0.01% | 0.00% | 0.01% | 0.01%
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
-0.02% | -0.03% | 0.03% | -0.01% | 0.00% | -0.05%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
-0.02% | 0.06% | 0.04% | -0.01% | -0.05% | 0.19%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.00% | -0.11% | -0.06% | 0.00% | 0.19% | -0.02%

## Slide 11: Simulation results – Setting B (Normal QP)
All Intra Main |  |  | All Intra HE10 |  | 
Y | U | V | Y | U | V
0.03% | 0.07% | 0.07% | 0.04% | 0.02% | 0.07%
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
0.04% | 0.03% | 0.11% | 0.05% | -0.02% | -0.07%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
0.04% | -0.23% | -0.09% | 0.03% | -0.27% | 0.07%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.04% | -0.07% | -0.27% | 0.03% | 0.37% | -0.32%

## Slide 12: Simulation results – Setting B (low QP)
All Intra Main |  |  | All Intra HE10 |  | 
Y | U | V | Y | U | V
0.01% | 0.03% | 0.01% | 0.02% | 0.01% | 0.02%
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
-0.01% | 0.00% | 0.04% | 0.00% | 0.02% | -0.03%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
0.00% | -0.13% | -0.04% | 0.01% | -0.11% | 0.02%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.01% | 0.02% | -0.07% | -0.03% | 0.23% | -0.25%

## Slide 13: Conclusions
Proposed equation based context derivation for LAST coding
  Remove the context mapping table
  Unify context derivation of luma and chroma
  Perform consecutive and sequential context fetching
0.0% Y BD-rate change
Recommend adoption of the proposed equation based context derivation
  Preferably with parameter setting A
Thanks to Samsung (JCTVC-I0477) for cross-checking

## Slide 14
Thank you!