## Slide 1: AHG11: Proposed text for sub-picture based CPB operation (JCTVC-I0333)
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
9th JCT-VC Meeting

## Slide 2: Outline
Draft text for sub-picture based CPB operation
  Per mandate 4 of AHG11 (High-level syntax)
  Purpose: interoperable ultra low-delay video transmission
Enhancement in Annex C
  Arrival time and removal time of sub-picture
  Bitstream conformance: definition of overflow at sub-picture level
New syntax in vui_parameters()
  sub_pic_cpb_flag: enabling flag of sub-picture based CPB operation
  num_ctbs_in_subpicture_minus1: specifies the size of each sub-picture
  removal_time_offset_length:
  picture_interval:
New syntax in hrd_parameters()
  removal_time_offset: allows fluctuation of bits in each sub-picture

## Slide 3: Sub-picture based CPB operation
Picture based removal time in AVC’s CPB
  A decoder can not start the decoding process of a picture before its removal time since the last bit of the first CTB might arrive at its removal time.
  Codec delay cannot be less than 1-frame period.
    Typically it takes 1-frame period to decode a picture.
Proposed sub-picture based removal time (explicitly signalled)
  Sub-picture: a set of treeblocks (i.e. a treeblock row)
    The number of bits in each sub-picture is controlled to be averaged.
  Codec delay is proportional to the size of a sub-picture.

## Slide 4: Signalling of sub-picture’s removal time
Original proposal (JCTVC-G188)
  M (the number of sub-pictures in a picture) is signalled.
    ( L % M ) shall be zero, where L = ( PicWidthInCtbs * PicHeightInCtbs )
  Nominal removal time of sub-picture m [0, M-1] in picure n: tr,n( n, m ) = tr,n( n - 1 ) + ( S * ( m + 1 ) / M ) , where S = ( tr,n( n ) – tr,n( n - 1 ) )
Improved definition
  N ( = num_ctbs_in_subpicture_minus1 + 1 ) is signalled.
    Ceil( L / N ) = M
    All sub-pictures except the last sub-picture contain N CTBs.
  ⊿t ( = removal_time_offset[ SchedSelIdx ] ) is signalled.
    ⊿t allows the fluctuation of #bits in each sub-picture.
    27 MHz precision
    Tr,n ( n, m ) = min( tr,n ( n ), tr,n ( n - 1 ) + ( S * ( m + 1 ) * M / N ) + removal_time_offset[ SchedSelIdx ] ÷ 27 000 000 )

## Slide 5: Syntax(1/2}
In vui_parameters()
if( vcl_hrd_parameters_present_flag ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag ¦ ¦ vcl_hrd_parameters_present_flag ) | 
sub_pic_cpb_flag | u(1)
if(sub_pic_cpb_flag != 0 ) { | 
num_ctbs_in_subpicture_minus1 | ue(v)
removal_time_offset_length | u(5)
picture_interval | ue(v)
} | 
low_delay_hrd_flag | u(1)
picture_interval is used to derive tr,n( -1 ) = ( tr,n( 0 ) - picture_interval * tc )

## Slide 6: Syntax(2/2)
In hrd_parameters()
time_offset_length | u(5)
if( sub_pic_cpb_ flag != 0){ | 
removal_time_offset | u(v)
} | 
} | 

## Slide 7: Discussions(1/2)
Definition of a sub-picture
  It is specified as a “decoding unit” in the proposed text.
  A decoding unit may not be a set of complete NAL units.
    If the size of a decoding unit is small, “a set of complete NAL units” constraint degrades coding efficiency since it forces to insert a slice header at the beginning of each decoding unit.
Compatibility with AVC-style CPB operation
  Sub-picture based removal time is defined in addition to picture based removal time.
  This spec does not force a decoder to perform sub-picture based CPB operation. (i.e. no changes in decoder conformance part)
Bitstream conformance
  The final arrival time of decoding unit (n, m) is specified as taf( n, m ) = tai( n ) + b( n, m ) ÷ BitRate[ SchedSelIdx ], where b( n, k ) is the size in bits of decoding unit from 0 up to k in access unit n
  taf( n, m ) shall be equal or less than tr( n, m )

## Slide 8: Discussions(2/2)
low_delay_hrd_flag
  The proposed text requires low_delay_hrd_flag = 0 when sub_pic_cpb_flag = 1, for the sake of simplicity.
  This constraint may be relaxed. But the important point is that the causality shall be considered for ultra low delay coding.
    An encoder firstly decides the values of parameters, then encodes so that generated bitstream conforms to the spec.
    An encoder should not change the parameters after encoding a picture. This introduces 1-frame period delay at the encoder side.
    An encoder cannot know the occurrence of a “big picture” prior to the beginning of picture processing.