## Slide 1: Proposed Fix on CBFY Inference at Minimum TU Size (JCTVC-I0334)
Liwei Guo, Marta Karczewicz

## Slide 2: Introduction
CBFY inference in HM6 for inter coding
  CBFY3 is inferred to be 1 when
    CBFU =CBFV =0 and CBFY0=CBFY1=CBFY2=0
  The inference does not cover all cases at MinTUSize
Proposed fix for CBFY inference at MinTUSize
  Increase the consistency of CBFY inference

## Slide 3: Proposed Fix
We use MinTUSize = 4x4 as example
If a unit (e.g., 8x8) is further split into units of MinTUSize,
  Split can only be performed to Y since both U and V already reach MinTUSize
  There must be at least one non-zero Y coefficient
    Y3 is referred to be 1 if Y0=Y1=Y2=0,
8
Y0
Y1
Y2
Y3
U
V
4

## Slide 4: Simulation results
No change in encoding time or decoding time is observed.
Common test condition.
Results averaged over all sequences including Class F.
Cross-checked by Microsoft (JCTVC-I0516).
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
0.01% | -0.03% | 0.02% | -0.01% | 0.01% | -0.02%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
-0.02% | -0.24% | 0.01% | -0.04% | -0.03% | 0.04%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.00% | -0.08% | -0.21% | -0.03% | 0.36% | 0.11%

## Slide 5
Thank you!

## Slide 6: Detail results (1)
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.06% | 0.00% | 0.07% | 0.03% | 0.22% | 0.10%
Class B | 0.00% | -0.01% | 0.07% | -0.01% | -0.01% | 0.02%
Class C | -0.01% | -0.02% | -0.07% | -0.02% | 0.04% | -0.12%
Class D | 0.01% | -0.18% | 0.06% | -0.01% | -0.17% | -0.13%
Class E |  |  |  |  |  | 
Class F | 0.00% | 0.02% | -0.03% | -0.04% | -0.01% | 0.03%
Overall | 0.01% | -0.03% | 0.02% | -0.01% | 0.01% | -0.02%
 | 0.01% | -0.04% | 0.01% | -0.01% | 0.03% | -0.02%
Enc Time[%] | 99.64% |  |  | 100.25% |  | 
Dec Time[%] | 98.45% |  |  | 98.58% |  | 

## Slide 7: Detail results (2)
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.02% | -0.26% | 0.00% | -0.01% | 0.06% | 0.13%
Class C | 0.00% | -0.04% | -0.23% | -0.05% | 0.15% | 0.00%
Class D | 0.02% | -0.40% | 0.21% | -0.01% | -0.12% | -0.32%
Class E | 0.05% | -0.37% | 0.27% | -0.05% | -0.35% | 0.10%
Class F | -0.12% | -0.15% | -0.15% | -0.09% | 0.03% | 0.27%
Overall | -0.02% | -0.24% | 0.01% | -0.04% | -0.03% | 0.04%
 | -0.02% | -0.21% | 0.04% | -0.04% | -0.02% | 0.00%
Enc Time[%] | 101.47% |  |  | 99.30% |  | 
Dec Time[%] | 100.55% |  |  | 98.58% |  | 

## Slide 8: Detail results(3)
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.05% | -0.13% | -0.30% | -0.01% | 0.16% | -0.20%
Class C | -0.01% | -0.25% | -0.12% | 0.00% | 0.02% | -0.18%
Class D | 0.02% | 0.31% | -0.16% | -0.07% | 0.41% | -0.20%
Class E | -0.06% | -0.37% | 0.21% | 0.00% | 0.43% | -0.09%
Class F | -0.01% | -0.04% | -0.52% | -0.05% | 0.87% | 1.26%
Overall | 0.00% | -0.08% | -0.21% | -0.03% | 0.36% | 0.11%
 | 0.01% | -0.11% | -0.21% | -0.03% | 0.35% | 0.19%
Enc Time[%] | 99.42% |  |  | 99.30% |  | 
Dec Time[%] | 101.99% |  |  | 98.38% |  |