## Slide 1: Proposed Fix on CBFY Inference at Minimum TU Size (JCTVC-I0334)
Liwei Guo, Marta Karczewicz

## Slide 2: Introduction
CBFY inference in HM6 for inter coding
  CBFY3 is inferred to be 1 when
    CBFU =CBFV =0 and CBFY0=CBFY1=CBFY2=0
  The inference does not cover all cases at MinTUSize
Proposed fix for CBFY inference at MinTUSize:
  Increased chance of CBFY inference
  No change in RD performance

## Slide 3: Proposed Fix
We assume MinTUSize = 4x4
If a unit (e.g., 8x8) is further split into MinTUSize,
  Split can only be performed to Y since UV already reaches MinTUSize
  There must be at least one non-zero Y coefficient
    Y3 is referred to be 1 if Y0=Y1=Y2=0,
8
Y0
Y1
Y2
Y3
U
V
4

## Slide 4: Simulation results
No increase in encoding time or decoding time is observed.
Common test condition.
Results averaged over all sequences including Class F.
Cross-checked by Microsoft.
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
0.01% | -0.03% | 0.02% | -0.01% | 0.01% | -0.02%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
-0.02% | -0.24% | 0.01% | -0.04% | -0.03% | 0.04%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
0.00% | -0.08% | -0.21% | -0.03% | 0.36% | 0.11%

## Slide 5: Conclusions
Refine the condition for CBFY inference at MinTUSize in inter coding
  Increased chance of CBFY inference
  No change in performance compared to HM6
Recommend adoption of the proposed fix
Thanks to Microsoft (JCTVC-I0516) for cross-checking

## Slide 6: Detail results (1)
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.06% | 0.00% | 0.07% | 0.03% | 0.22% | 0.10%
Class B | 0.00% | -0.01% | 0.07% | -0.01% | -0.01% | 0.02%
Class C | -0.01% | -0.02% | -0.07% | -0.02% | 0.04% | -0.12%
Class D | 0.01% | -0.18% | 0.06% | -0.01% | -0.17% | -0.13%
Class E |  |  |  |  |  | 
Class F | 0.00% | 0.02% | -0.03% | -0.04% | -0.01% | 0.03%
Overall | 0.01% | -0.03% | 0.02% | -0.01% | 0.01% | -0.02%
 | 0.01% | -0.04% | 0.01% | -0.01% | 0.03% | -0.02%
Enc Time[%] | 99.64% |  |  | 100.25% |  | 
Dec Time[%] | 98.45% |  |  | 98.58% |  | 

## Slide 7: Detail results (2)
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.02% | -0.26% | 0.00% | -0.01% | 0.06% | 0.13%
Class C | 0.00% | -0.04% | -0.23% | -0.05% | 0.15% | 0.00%
Class D | 0.02% | -0.40% | 0.21% | -0.01% | -0.12% | -0.32%
Class E | 0.05% | -0.37% | 0.27% | -0.05% | -0.35% | 0.10%
Class F | -0.12% | -0.15% | -0.15% | -0.09% | 0.03% | 0.27%
Overall | -0.02% | -0.24% | 0.01% | -0.04% | -0.03% | 0.04%
 | -0.02% | -0.21% | 0.04% | -0.04% | -0.02% | 0.00%
Enc Time[%] | 101.47% |  |  | 99.30% |  | 
Dec Time[%] | 100.55% |  |  | 98.58% |  | 

## Slide 8: Detail results(3)
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.05% | -0.13% | -0.30% | -0.01% | 0.16% | -0.20%
Class C | -0.01% | -0.25% | -0.12% | 0.00% | 0.02% | -0.18%
Class D | 0.02% | 0.31% | -0.16% | -0.07% | 0.41% | -0.20%
Class E | -0.06% | -0.37% | 0.21% | 0.00% | 0.43% | -0.09%
Class F | -0.01% | -0.04% | -0.52% | -0.05% | 0.87% | 1.26%
Overall | 0.00% | -0.08% | -0.21% | -0.03% | 0.36% | 0.11%
 | 0.01% | -0.11% | -0.21% | -0.03% | 0.35% | 0.19%
Enc Time[%] | 99.42% |  |  | 99.30% |  | 
Dec Time[%] | 101.99% |  |  | 98.38% |  | 

## Slide 9
Thank you!