## Slide 1: I0350: Splitting contexts for MVD coding Vadim Seregin, Jianle Chen, Xianglin Wang and Marta Karczewicz
Notes: Preparation for the 8-th JCT-VC meeting
Possible topics to look into (JS)

## Slide 2: Background
MVD syntax coding in current HM
  MVD parsing is skipped for list L1 if mvd_l1_zero_flag is enabled
    MVD is set to zero
  For signaled MVD, context models are shared among
    lists L0 and L1
    Uni-predicted PU and bi-predicted PU
Problem
  MVD parsing skip can not be applied to L0
  Adaptation only at slice level using mvd_l1_zero_flag
  MVD bins from different lists may have different statistical properties

## Slide 3: Proposed method
Separate the context model of L0 and L1 MVD of bi-predicted PU
  One for uni, one for bi-L0 and one for bi-L1 (two contexts added)
Benefits
  No high level syntax needed
  No change to MVD parsing
  Automatically accommodate different ME design at encoder side
 | RA-Main | RA-HE10 | LB-Main | LB-HE10
Proposed method | 0.06 | 0.06 | 0.03 | 0.00

## Slide 4: Proposed method with adaptation
CU based adaptive selection between zero and non-zero MVD for list L1
 | RA-Main | RA-HE10 | LB-Main | LB-HE10
Zero/Non-zero L1 MVD with separate contexts | -0.06 | -0.05 | -0.29 | -0.28
Zero/Non-zero L1 MVD without separate contexts | -0.06 | -0.04 | 0.04 | 0.08

## Slide 5
Thank you!