## Slide 1: AHG7: Motion vector rounding for the worst case bandwidth reduction Vadim Seregin, Xianglin Wang, Jianle Chen and Marta Karczewicz
Notes: Preparation for the 8-th JCT-VC meeting
Possible topics to look into (JS)

## Slide 2: Introduction
Reference pixels for 2D interpolation in MC
Issue: High bandwidth requirement, especially for small blocks
Solution: MV rounding to integer pel position

## Slide 3: Motion vector rounding
Rounding is done to nearest integer
  MV = ( Sign(MV) ∙ ( abs( MV ) + 1 ) >> 2 )
Applied to 8x4 and 4x8 bi-predicted PUs
  Round vertical component, MVy, for both MVs
  Signal corresponding MVD = MVD >> 2
 | RA-Main | RA-HE10 | LB-Main | LB-HE10
Rounding for 8x4 and 4x8 | 0.1 | 0.1 | 0.1/0.2 | 0.1/0.2
Chart: 
| 8x4 | 8x8
Anchor | 14.7 | 10.1
Reduction | 9.9
33%

## Slide 4: Motion vector rounding
Applied for 8x4, 4x8 and 8x8 bi-predicted PUs
  For 8x4 and 4x8 PUs
    Round both MVs
  For 8x8 PU
    Round vertical component for both MVs
  Signal corresponding MVD = MVD >> 2

## Slide 5: Bandwidth reduction
 | RA-Main | RA-HE10 | LB-Main | LB-HE10
Case 1. Rounding for 8x4 and 4x8 | 0.1 | 0.1 | 0.1 | 0.1
Case 2. Rounding for 8x4, 4x8 and 8x8 | 0.4 | 0.3 | 0.5 | 0.4
Chart: 
| 8x4 | 8x8 | 16x8
Anchor | 14.7 | 10.1 | 7.8
Reduction | 9.9 | 6.8
33%
54%

## Slide 6
Thank you!