## Slide 1: JCTVC-I0362: Virtual Line Buffer Model and Restriction on Asymmetric Tile Configuration
Sanjeev Kumar, Geert Van der Auwera,
Ye-Kui Wang, Muhammed Coban,
Marta Karczewicz

## Slide 2: Summary
Asymmetric tile configurations have line buffer size penalty for loop filtering compared to symmetric tile configurations
It is proposed to restrict asymmetry of tile configurations in order to reduce line buffer requirement to that for symmetric tile configurations
Through constraints on column_width, row_height of tiles for two cases: vertical tiles and tile arrays (not for horizontal tiles or no tiles)
For 4k x 2k picture, line buffer savings are more than 6KB.

## Slide 3: Tile Configurations and Line Buffer Sizes
Asymmetric tiles are supported in HEVC Main profile
  minimum tile width = 384
Line buffer sizes for different tile configurations:
  Case-1. No tiles
    Total line buffer size 1 + picture_width / LCU_size
  Case-2. Only horizontal tiles
    Num_tile_columns = 1
    Num_tile_rows > 1
    Total line buffer size 1 + picture_width / LCU_size

## Slide 4: Tile Configurations and Line Buffer Sizes
  Case-3. Only vertical tiles
    Num_tile_columns > 1
    Num_tile_rows = 1
    Total line buffer size 1 + (max_tile_width + picture_height) / LCU_size
  Case-4. Tile array (both horizontal and vertical tiles)
    Num_tile_columns > 1
    Num_tile_rows > 1
    Total line buffer size 1 + (picture_width + max_tile_height) / LCU_size

## Slide 5: Tile Configurations and Line Buffer Sizes
It is proposed to use line buffer size for the two worst case symmetric tile configurations (2x2 and 2x1) as the “Total virtual line buffer size” (picture_width >= picture_heigth and picture_width < picture_height cases are considered):
“Total virtual line buffer size” max(picture_width,picture_heigth)/LCU_size + min(picture_width,picture_height)/(2*LCU_size) + 1
Only cases 3 and 4 can have larger line buffer sizes than worst symmetric cases
It is proposed to apply the “Total virtual line buffer size” as upper bound for cases 3 and 4

## Slide 6: Proposed Constraints
It is a requirement of bit stream conformance that if tiles_or_entropy_coding_sync_idc = 1 and uniform_spacing_flag = 0, then values of row_width[i] and column_width[i] shall satisfy following conditions for all valid i:
If num_tile_columns_minus1 > 0 and num_tile_rows_minus1 = 0 (case 3)
384>>Log2CtbSize
<=
column_width[i]
<=
max( 384>>Log2CtbSize, max(PicWidthInCtbs, PicHeightInCtbs) +
min(PicWidthInCtbs, PicHeightInCtbs)>>1 – PicHeightInCtbs )
If num_tile_columns_minus1 > 0 and num_tile_rows_minus1 > 0 (case 4)
row_height[i]
<=
max(PicWidthInCtbs, PicHeightInCtbs)
+ min(PicWidthInCtbs, PicHeightInCtbs)>>1 – PicWidthInCtbs

## Slide 7: Conclusion
It is proposed to restrict the asymmetry of tile configuration to reduce loop filter line buffer requirement for Deblocking, Sample Adaptive Offset and Adaptive Loop Filter such that total line buffer size does not exceed symmetric tile configuration worst case buffer sizes.
Constraints on tile column_width (vertical tiles only) or tile row_height (tile array)
For 4k x 2k picture, line buffer savings are more than 6KB.