## Slide 1
<number>
JCTVC-I0392: Segment Based Weak Filtering Decision
Faouzi Kossentini
9th JCTVC Meeting, Geneva. CH
April 27th - May 7th 2012
Notes: <number>

## Slide 2: Motivation
Almost all DLF decisions are segment-based.
In weak filtering, the decision on whether to filter the first samples on either side of the 4-sample-edge is line-based.
By making this weak filtering decision segment-based, we will simplify the DLF decision.
<number>

## Slide 3: HM 6.0 Weak Filtering Decision Process
<number>
Filtering of q0i and p0i
  Decision taken based on Δ calculated for each line
  Comparing Δ to 10*tc , with tc being the same for all 4 lines
Line-based decision
2. Filtering of q1i and p1i
  At each line, if q0i and p0i are filtered,  Line-based decision
  Another decision is taken based on the β, dq and dp values that are the same for the 4 lines  Segment-based decision
SAMPLE LINES USED
FOR DECISION
LINE-BASED DECISION
LINE-BASED DECISION && SEGMENT-BASED DECISION
Notes: <number>

## Slide 4: Proposed Weak Filtering Decision Process
<number>
Weak filtering decisions:
Filtering of q0i and p0i
  Decision taken based on Δ0 and Δ3 calculated using samples from the first and fourth lines.
  Comparing Δ (average of Δ0 and Δ3) to 10*tc , with tc depending on β which is the same for all 4 lines
 Segment-based decision
2. Filtering of q1i and p1i
  At each segment, if q0i and p0i are filtered,  Segment-based decision
  Another decision is taken based on the β, dq and dp values that are the same for the 4 lines
 Segment-based decision
SAMPLE LINES USED
FOR DECISION
SEGMENT-BASED DECISION
Notes: <number>

## Slide 5: Simulation Results for Main Configurations
<number>
Low delay P Main |  |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.2% | -0.2%
Class C | 0.0% | -0.4% | 0.0%
Class D | 0.0% | -0.3% | -0.5%
Class E | -0.1% | 0.2% | 0.5%
Class F | 0.0% | -0.4% | -0.3%
Overall | 0.0% | -0.2% | -0.1%
Low delay B Main |  |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.3% | 0.0%
Class C | 0.0% | 0.1% | 0.0%
Class D | 0.0% | -0.5% | 0.2%
Class E | 0.1% | 0.1% | 0.4%
Class F | -0.1% | 0.1% | -0.4%
Overall | 0.0% | -0.1% | 0.0%
All Intra Main |  |  | 
 | Y | U | V
Class A | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
Random Access Main |  |  | 
 | Y | U | V
Class A | 0.0% | 0.1% | 0.1%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | -0.1% | 0.0%
Class E |  |  | 
Class F | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%

## Slide 6: Simulation Results for HE_10 Configuration
<number>
Random Access HE_10 |  |  | 
 | Y | U | V
Class A | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | -0.1%
Class D | 0.0% | 0.0% | -0.1%
Class E |  |  | 
Class F | 0.0% | -0.1% | 0.0%
Overall | 0.0% | 0.0% | 0.0%

## Slide 7: Subjective Evaluation: Conditions
<number>
Equipment and room conditions:
  42”, 1080p, Viera-class Panasonic plasma monitor
  Subjects sat 2 to 4 feet from the monitor
  Viewing angle never exceeded 45 degrees
  Darkened room
Video sequences were:
  Presented side-by-side
  Presented in a randomized single blinded manner
  Displayed at native size
  Played twice in immediate succession with five-to-ten second pauses between presentations
Notes: <number>

## Slide 8: Subjective Quality Results
<number>
Sequence | Number of viewers | HM-6.0 | Proposed | No Preference | Remarks
BQMall | 6 | 2 | 3 | 1 | Four viewers noted that the proposed version is slightly better or the same as the anchor.
 |  | 33% | 50% | 17% | 
Cactus | 6 | 1 | 4 | 1 | Five viewers noted that the proposed version is slightly better or the same as the anchor.
 |  | 17% | 66% | 17% | 
Four People | 6 | 1 | 2 | 3 | Five viewers noted that the proposed version is slightly better or the same as the anchor.
 |  | 17% | 33% | 50% | 
Kimono | 6 | 0 | 4 | 2 | Six viewers noted that the proposed version is slightly better or the same as the anchor.
 |  | 0% | 66% | 33% | 
RaceHorsesC | 6 | 4 | 1 | 1 | Four viewers noted that the anchor is slightly worse than the proposed version
 |  | 66% | 17% | 17% | 
Total | 30 | 8 | 14 | 8 | Overall, 73% either preferred the proposed version or expressed no clear preference.
 | 100% | 27% | 46% | 27% | 
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 9: Conclusions
<number>
DLF decision process all segment-based
Complexity relative to HM 6.0:
  Similar coding efficiency levels
  Simplifying the decision process
  Decrease in complexity
Improved subjective overall quality.