## Slide 1: Tree syntax for field sequence SEI
Geneva
April 2012
JCTVC I-393

## Slide 2: First, to clear the air..
No one in their right mind would use interlace for new captures, transport, display formats.
In fact, interlace “sucks” so bad, light cannot escape ..or at least every other line…
..but, it is needed for legacy sources
interlace sucks – interlace sucks – interlace sucks -- interlace sucks – interlace sucks – interlace sucks –interlace sucks
progressive
interlaced

## Slide 3: Core concept example: PAFF -> field seq.
Top Bot
Top Bot Top
Bot Top
frame
Bot Top Bot
Source
(example: mixed content.. An extreme case)
Picture numbers are to show mapping from source to field input to encoder.. It is not POC, frame_num, etc.
Transport & encoding
(all fields in a field sequence)
field_sequence_flag=1
1
2
3
4
5
6
7
8
9
10
11
Top Bot
12
13
1 1 2 3 4 5 6 7 8 9 10 11 12 13
Progressive frame
3:2 epoch
Some pure field pictures
progressive_source_flag=1
progressive_source_flag=0
Pre-mux prior to HEVC encode
duplicate_flag=1
Top Bot Top Bot Top Bot Top Bot Top Bot Top Bot Top Bot
bottom_field_flag
1 2&3 4&5 7&8 9&10 12 13
Progressive display
deinterlaced
Re-interleaved
Re-interleaved
Re-interleaved,
#6 duplicate dropped
Re-interleaved,
#11 duplicate dropped
Re-interleaved

## Slide 4: Key, independent flags in field SEI
field_sequence_flag: how fields/frames are packed for transport through HEVC codec
progressive_source_flag: indicates whether content is progressive or interlaced
duplicate_flag: indicates coded picture is duplicated / can be dropped

## Slide 5: Benefits of the current SEI
Pass-through concept that allows mixed progressive & interlace content to tunnel through HEVC without changes to Video Coding Layer (VCL), including HRD (no phantom/non-existent pictures in HRD!)
Signals content type (interlaced or progressive via progressive_source_flag) separately from picture structure transport (field or frame pictures via field_sequence_flag)
Pure interlaced can be sent cleanly as field sequences.
For fixed equipment, such as those linked by SDI (e.g. HD-D5), fields can be encapsulated (interleaved) in frames, or progressive frames can be encapsulated (extracted) in fields, then re-assembled back into source format according to the SEI flags.
Duplicate_flag identifies coded pictures that were synthesized by, for example, stream splicing, editing, or 3:2 pulldown
HEVC
fields
frames
frames
fields
SEI metadata
SEI metadata

## Slide 6: The current SEI: flag vector style section D.1.19 of HEVC CD (I-0030)
field_indication( payloadSize ) { | Descriptor
sequence_type_flag | u(1)
progressive_source_flag | u(1)
bottom_field_flag | u(1)
top_field_first_flag | u(1)
duplicate_flag | u(1)
reserved_zero_3bits /* equal to 0 */ | u(3)
} | 

## Slide 7: Basic four cases (D.2.19)

## Slide 8: Problem: some combinations are not meaningful (indicated by “X”)
Use case | field_sequence | progressive_source | bottom_field | top_field_first
Interleaved fields, bottom field output first | 0 | 0 | X | 0
Interleaved fields, top field output first | 0 | 0 | X | 1
(pure progressive) frame | 0 | 1 | X | X
Top field picture (pure interlaced) | 1 | 0 | 0 | X
Bottom field picture (pure interlaced) | 1 | 0 | 1 | X
Top field extracted from a progressive frame | 1 | 1 | 0 | X
Bottom field extracted from a progressive frame | 1 | 1 | 1 | X

## Slide 9: Meaningful use cases
sequence
frame seq
bottom
first
prog
frame
field seq
field picture
progressive_source_flag
bottom_field_flag
top_field_first_flag
top
first
inter-leaved
extracted field
Top
field_sequence_flag
Bottom
Top
Bottom
X
X
X
X
X
0
1
1
1
1
1
1
0
0
0
0
0

## Slide 10: Observations
top_field_first and bottom_field are mutually exclusive:
  bottom_field (field parity) always needed in field sequences (field_sequence_flag==1) to signal field parity; bottom_field is not meaningful in frame sequences (field_sequence_flag==0).
  top_field_first only needs to be signalled in frame sequences containing interlaced content (field_sequence_flag==0 && progressive_source_flag==0), the so-called “interleaved fields,” to know which interleaved field (top or bottom) should be output first
  Neither top_field_first nor bottom_field needed in pure progressive frame sequences (field_sequence_flag==0 && progressive_source_flag==1)
Possible solution: eliminate combinations that are not meaningful by making them impossible to signal via a conditional tree syntax, thus helping HEVC specification readers from harming themselves.

## Slide 11: Tree version syntax (no functional changes to current SEI)
field_sequence_flag
progressive_source_flag
duplicate_flag
top_field_first
bottom_field
SEI
field_sequence_flag?
No
Yes
No
Yes
Interleaved fields
progressive_source_flag?
reserved_zero_1bit
Frame sequences
Field sequences
Pure progressive
frames

## Slide 12: Proposed syntax
field_indication( payloadSize ) { | Descriptor
field_sequence_flag | u(1)
progressive_source_flag | u(1)
duplicate_flag | u(1)
if( field_sequence_flag==1 ) | 
bottom_field_flag | u(1)
else if( progressive_source==0) | 
top_field_first_flag | u(1)
else | 
reserve_zero_1bit | u(1)
reserved_zero_4bits /* equal to 0 */ | u(4)
} |