## Slide 1: I0394: Copy Slice Type
Sachin Deshpande, Andrew Segall
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Proposal
HEVC CD supports three slice types - I Slice, P Slice, B Slice.
We propose a new slice_type – C (Copy Slice).
The proposed Copy slice type allows very low overhead for signaling that a slice from one frame is a copy of a slice from other frame.
<number>
Notes: <number>

## Slide 3: Use Cases for Copy Slice Type
Use Cases where Copy Slice is useful for efficiently signaling:
A slow motion video sequence coded with frame replication: In this case each frame is repeated two or more times. The proposed copy Slice type can signal the repeated frames efficiently.
A simple frame rate upsampler with frame repeat: In LCD televisions a frame rate upsampler may be used to generate higher frame rate sequence from original frame rate sequence (e.g. 60 Hz -> 120Hz). A simple frame rate up-converter may double the frame rate of the video by simply repeating each frame. In some cases this higher frame rate video may be already encoded and transmitted as a 120 Hz video bitstream. In this case the proposed copy slice type can be used for efficient coding of repeated frames.
2-UP Videos with static background: In certain news video segments video of news anchor and a reporter may be shown in 2 windows side by side with static background at the top and bottom of the overall video window. In this case if multiple slices are used per frame a Copy slice type can be used to efficiently code entire slice (at the top/ bottom) as a copy of collocated slice from previous frame.
<number>

## Slide 4: Proposed Syntax and Semantics : Slice Header
When slice_type is 3 the slice is of type C, i.e. copy slice. In this case following syntax elements are present.
copyslice_delta_poc_sign specifies the sign of copyslice_delta_poc_minus1. A value of 0 indicates that the sign is positive and a value of 1 indicates that the sign is negative.
copyslice_delta_poc_minus1 plus 1 specifies an absolute difference between two picture order count values. The value of copyslice_delta_poc_minus1 shall be in the range of 0 to 215 − 1, inclusive.

## Slide 5: Results
Test Condition: Low Delay P Main Configuration
Video: With successive pictures repeated
Bit Count for repeated pictures:

## Slide 6: Proposal
The document proposed syntax and semantics for a new slice_type – C (Copy Slice).
The proposed Copy slice type allows improved coding efficiency when a slice from one frame is a copy of a slice from other frame.
We propose to adopt the proposed approach in HEVC.
<number>