## Slide 1: Intra Transform Skipping
Cuiling Lan, Jizheng Xu, Gary J. Sullivan, Feng Wu
Xidian University
Microsoft Corp.

## Slide 2: Summary
Intra transform skipping for 4x4 TUs
  No change to prediction, entropy coding, in-loop filtering, scaling and quantization
All intra coding, class F
  7.8% bit-saving (30% enc time increase)
  7.3% bit-saving (14% enc time increase)
RA, LD coding, class F
  5.6% for RA, 3.4% for LD, without noticeable enc time change
No decoding time increase

## Slide 3: Background
Vision, Applications and Requirements for High Efficiency Video Coding (HEVC)
  HEVC shall support encoding of text and graphics mixed into a camera-captured video source, rendered animation content, rendered computer graphics, computer desktop or mobile device display content, scrolling text over camera-captured video
Improvement on class F sequences seems to be lower
Comparison between HM6 and JM18.3
  Low delay B
Simple modification to improve coding efficiency for class F sequences is desired.
  JCTVC-H0361 CE5.f: Residual Scalar Quantization for HEVC
 | Y | U | V
Class A |  |  | 
Class B | −42.0% | −30.1% | −30.4%
Class C | −32.3% | −27.6% | −26.6%
Class D | −29.2% | −28.4% | −30.0%
Class E | −43.1% | −32.5% | −31.1%
Class F | −29.2% | −25.0% | −25.2%
Average | −35.1% | −28.6% | −28.6%

## Slide 4: Proposed transform skipping design
Transform skipping for intra TUs
  For both luma and chroma TUs
  Only apply to 4x4 intra TUs
No change to prediction, de-quantization, scaling, deblocking, SAO, ALF.
Transform is skipped. A scaling down process is used instead.

## Slide 5: Transform skipping on TUs with different sizes
 | All Intra Main |  |  | All Intra HE10 |  |  |  | 
 | Y | U | V | Y | U | V | Enc Time[%] | Dec Time[%]
TS for 4x4-32x32 TUs | -8.3% | -8.1% | -9.0% | -8.3% | -7.6% | -8.4% | 175% | 100%
TS for 4x4-16x16 TUs | -8.3% | -8.0% | -9.0% | -8.2% | -7.6% | -8.3% | 161% | 99%
TS for 4x4 and 8x8 TUs | -8.2% | -7.9% | -8.6% | -8.1% | -7.2% | -7.8% | 149% | 99%
TS for 4x4 TUs | -7.8% | -7.6% | -8.3% | -7.7% | -7.1% | -7.8% | 130% | 101%
Thanks to MERL for cross-verification (JCTVC-I0417)

## Slide 6: TS for 4x4 TUs
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2%
Class B | 0.0% | -0.1% | -0.4% | 0.0% | 0.0% | -0.4%
Class C | 0.0% | -0.1% | -0.3% | -0.1% | -0.1% | -0.2%
Class D | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | -0.3%
Class E | 0.1% | 0.0% | -0.7% | 0.1% | -0.1% | -0.5%
Overall | 0.0% | -0.1% | -0.4% | 0.0% | 0.0% | -0.3%
 | 0.0% | -0.1% | -0.4% | 0.0% | 0.0% | -0.3%
Class F | -7.8% | -7.6% | -8.3% | -7.7% | -7.1% | -7.8%
Enc Time[%] | 130% |  |  | 129% |  | 
Dec Time[%] | 101% |  |  | 102% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.2% | -0.5% | 0.0% | 0.0% | -0.4%
Class B | 0.1% | -0.2% | -0.3% | 0.0% | -0.1% | -0.5%
Class C | -0.1% | -0.3% | -0.5% | -0.1% | -0.2% | -0.3%
Class D | 0.0% | -0.2% | -0.4% | 0.0% | -0.3% | -0.6%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.2% | -0.4% | 0.0% | -0.1% | -0.5%
 | 0.0% | -0.2% | -0.5% | 0.0% | -0.1% | -0.5%
Class F | -5.6% | -6.6% | -6.9% | -5.5% | -6.4% | -6.9%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.3% | -0.3% | 0.0% | 0.0% | 0.1%
Class C | 0.0% | 0.3% | 0.0% | 0.0% | 0.4% | 0.2%
Class D | 0.1% | 0.3% | 0.3% | 0.1% | -0.2% | 0.3%
Class E | -0.1% | -1.0% | -0.5% | -0.1% | -0.1% | -1.3%
Overall | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.2%
Class F | -3.4% | -3.9% | -4.9% | -3.0% | -2.5% | -3.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.1% | 0.0% | -0.1% | 0.0% | 0.2% | 0.0%
Class C | 0.0% | -0.2% | -0.2% | 0.0% | 0.1% | -0.2%
Class D | 0.1% | 0.5% | -0.4% | 0.1% | 0.6% | 0.5%
Class E | -0.1% | -0.8% | -0.6% | 0.2% | 1.2% | -0.6%
Overall | 0.0% | -0.1% | -0.3% | 0.1% | 0.5% | 0.0%
 | 0.0% | -0.1% | -0.3% | 0.1% | 0.4% | 0.0%
Class F | -3.2% | -3.6% | -5.2% | -3.1% | 0.1% | -5.3%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 

## Slide 7: TS for 4x4 TUs + fast encoding
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
Class C | -0.1% | 0.3% | 0.3% | -0.1% | 0.2% | 0.3%
Class D | 0.0% | 0.3% | 0.3% | 0.0% | 0.3% | 0.3%
Class E | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Overall | 0.0% | 0.2% | 0.2% | 0.0% | 0.2% | 0.2%
 | 0.0% | 0.2% | 0.2% | 0.0% | 0.2% | 0.2%
Class F | -7.3% | -5.5% | -5.4% | -7.3% | -5.7% | -5.5%
Enc Time[%] | 114% |  |  | 113% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.1% | 0.0% | 0.0% | 0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.3% | 0.0% | 0.0% | 0.2%
Class C | -0.1% | 0.2% | 0.2% | -0.1% | 0.2% | 0.2%
Class D | 0.0% | 0.0% | 0.3% | 0.0% | 0.4% | 0.3%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.2% | 0.0% | 0.2% | 0.1%
 | 0.0% | 0.1% | 0.2% | 0.0% | 0.2% | 0.2%
Class F | -5.2% | -3.9% | -3.7% | -5.0% | -4.2% | -4.1%
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | 0.3%
Class C | 0.0% | 0.2% | 0.0% | 0.0% | 0.3% | 0.2%
Class D | 0.1% | 0.2% | 0.4% | 0.1% | 0.0% | 0.4%
Class E | 0.0% | -0.5% | 0.4% | 0.0% | 0.3% | 0.3%
Overall | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.3%
 | 0.0% | -0.1% | 0.2% | 0.0% | 0.1% | 0.2%
Class F | -3.0% | -2.9% | -2.9% | -2.8% | -1.3% | -2.9%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.3% | 0.0% | 0.1% | 0.2% | 0.2%
Class C | 0.0% | -0.4% | -0.2% | 0.0% | 0.2% | 0.0%
Class D | 0.1% | 0.1% | -0.7% | 0.1% | 0.5% | 0.2%
Class E | 0.1% | -0.1% | 0.4% | 0.2% | 0.8% | 0.8%
Overall | 0.1% | 0.0% | -0.2% | 0.1% | 0.4% | 0.3%
 | 0.1% | 0.0% | -0.1% | 0.1% | 0.4% | 0.4%
Class F | -2.9% | -2.6% | -2.8% | -2.7% | -2.1% | -2.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Thanks to TI for cross-verification (JCTVC-I0382)

## Slide 8: Visual comparison
BasketballDrillText AI_Main
  HM6: Qp37@4377.49Kbps YPSNR:32.52dB
  TS: Qp37@4429.25Kbps YPSNR:32.56dB
ChinaSpeed AI_Main
  HM6: Qp37@6903.70Kbps YPSNR:33.26dB
  TS: Qp36@6900.62Kbps YPSNR:34.36
SliceEditing RA_Main
  HM6: Qp37@608.42Kbps YPSNR:34.80dB
  RSQ: Qp36@600.87Kbps YPSNR:36.15dB

## Slide 9
HM6 AI_HE @Qp37 F400
TS AI_HE @Qp37 F400
BasketballDrillText AI_HE
  HM6: Qp37@4377.49Kbps YPSNR:32.52dB
  TS: Qp37@4429.25Kbps YPSNR:32.56dB

## Slide 10: ChinaSpeed AI_Main
HM6: Qp37@6903.70Kbps YPSNR:33.26dB
TS: Qp36@6900.62Kbps YPSNR:34.36

## Slide 11: HM6 AI_HE @Qp37 F140

## Slide 12: TS AI_HE @Qp36 F140

## Slide 13: ChinaSpeed AI_Main
HM6: Qp37@6903.70Kbps YPSNR:33.26dB
TS: Qp37@6382.36Kbps YPSNR:33.66
  7.6% bit-saving compared with HM6@Qp37

## Slide 14: HM6 AI_HE @Qp37 F140

## Slide 15: TS AI_HE @Qp37 F140

## Slide 16: SliceEditing RA_Main
HM6: Qp37@608.42Kbps YPSNR:34.80dB
TS: Qp36@600.87Kbps YPSNR:36.15dB

## Slide 17: HM6 RA_Main @Qp37

## Slide 18: TS RA_Main @Qp36

## Slide 19: SliceEditing RA_Main
HM6: Qp37@608.42Kbps YPSNR:34.80dB
TS: Qp37@569.59Kbps YPSNR:34.45dB
  6.4% bit-saving

## Slide 20: HM6 RA_Main @Qp37

## Slide 21: TS RA_Main @Qp37

## Slide 22: SlideShow RA_Main
HM6: Qp37@218.29Kbps YPSNR=39.20dB
TS: Qp37@217.31Kbps YPSNR=39.40dB

## Slide 23: HM6 RA_Main @Qp37

## Slide 24: TS RA_Main @Qp37

## Slide 25: Modifications
A transform skipping flag for each 4x4 intra TU
For TUs with transform skipping, transform is replaced by a right shift process (currently 4x4 transform also includes a right shift process).
  An alternative is to change the number of right shift in the scaling and quantization process and skip the transform module, as we proposed in JCTVC-H0361.

## Slide 26: Modifications – cont.
Method 1
Method 2
They are identical when QP>=6.

## Slide 27: Modifications – cont.
A flag in SPS to enable transform skipping
When transform skipping is enable, since we do not change the quantization process, we suggest to use a flat quantization matrix for intra 4x4 TUs.
  Small transform tends to have flat quantization
  Flat quantization is reasonable for spatial residues
  A single matrix for both intra 4x4 TUs
Or let the encoder decide how to better use quantization matrix and transform skipping simultaneously.

## Slide 28: Conclusions
Simple modification leads to significant objective/subjective improvement for class F sequences
Only impact 4x4 intra TUs, no change to other modules
Text modification and encoder description are ready
Propose adoption