## Slide 1: Comparison of Compression Performance of HEVC Draft 6 with AVC High Profile
Bin Li, Gary J. Sullivan, Jizheng Xu
University of Science and Technology of China Microsoft Corp.

## Slide 2: Performance Comparison
HEVC Draft 6 (HM-6.0)
AVC High Profile (JM-18.3)
PNSR based objective measurement
Further study of JCTVC-G399 and JCTVC-H0360

## Slide 3: Improved AVC Anchor
All Intra case and Random access AVC anchor are (almost) identical to that in JCTVC-H0360.
Low delay anchor is further improved
  1+3 reference picture setting
  B pictures instead of P pictures (Class E sequences are changed)
  Improve about 8% (Class E sequences are not considered) compared with the results in JCTVC-H0360.

## Slide 4: AVC High Profile vs. HEVC Draft 6 Main Profile
 | All Intra | Random Access | Low Delay
Class A | −23.4% | −36.9% | 
Class B | −22.7% | −39.4% | −40.3%
Class C | −20.1% | −30.1% | −31.5%
Class D | −16.9% | −28.3% | −29.2%
Class E | −28.6% |  | −41.2%
Class F | −22.3% | −26.2% | −28.8%
Average | −22.1% | −32.5% | −34.2%
Average without F | −22.0% | −34.0% | −35.5%

## Slide 5: AVC High Profile vs. HEVC Draft 6 High Efficiency 8-bit encoding
 | All Intra | Random Access | Low Delay
Class A | −26.9% | −41.2% | 
Class B | −24.7% | −42.5% | −42.7%
Class C | −22.4% | −33.3% | −34.4%
Class D | −18.2% | −31.5% | −31.6%
Class E | −30.2% |  | −44.5%
Class F | −25.0% | −29.0% | −32.7%
Average | −24.3% | −35.8% | −37.1%
Average without F | −24.2% | −37.4% | −38.2%

## Slide 6: HEVC Main Profile vs. HEVC High Efficiency 8-bit encoding
 | All Intra | Random Access | Low Delay
Class A | −4.7% | −7.3% | 
Class B | −2.6% | −5.4% | −4.4%
Class C | −3.1% | −4.8% | −4.5%
Class D | −1.7% | −4.6% | −3.4%
Class E | −2.4% |  | −5.9%
Class F | −3.6% | −3.9% | −5.6%
Average | −3.0% | −5.2% | −4.7%
Average without F | −2.9% | −5.5% | −4.5%
Enc. Time | 109% | 118% | 116%
Dec. Time | 113% | 114% | 108%

## Slide 7: HEVC “High Efficiency” Tools (excluding Class F “screen content”)
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV | Y | U | V | YUV
ALF | −1.3% | −0.4% | −0.4% | −1.1% | −3.2% | −1.4% | −1.4% | −2.9% | −1.8% | −1.3% | −1.1% | −1.7%
 | Enc./Dec. 105%/112% |  |  |  | Enc./Dec. 103%/116% |  |  |  | Enc./Dec. 101%/109% |  |  | 
LM | −0.7% | −7.5% | −5.7% | −1.8% | −0.2% | −9.4% | −6.4% | −1.4% | −0.1% | −2.7% | −2.1% | −0.5%
 | Enc./Dec. 104%/101% |  |  |  | Enc./Dec. 100%/101% |  |  |  | Enc./Dec. 100%/101% |  |  | 
AMP |  |  |  |  | −0.7% | −1.1% | −1.0% | −0.8% | −1.0% | −1.5% | −1.3% | −1.1%
 |  |  |  |  | Enc./Dec. 113%/100% |  |  |  | Enc./Dec. 113%/100% |  |  | 
NSQT |  |  |  |  | −0.3% | −0.8% | −0.6% | −0.4% | −0.8% | −2.4% | −1.9% | −1.1%
 |  |  |  |  | Enc./Dec. 102%/101% |  |  |  | Enc./Dec. 102%/101% |  |  | 

## Slide 8: HEVC High Efficiency 8-bit encoding vs. High Efficiency 10-bit encoding
 | All Intra | Random Access | Low Delay
Class A | −2.6% | −5.6% | 
Class B | −1.5% | −3.6% | −3.2%
Class C | −0.7% | −1.8% | −1.4%
Class D | −0.4% | −1.2% | −0.9%
Class E | −2.0% |  | −6.9%
Class F | −0.2% | −0.9% | −0.3%
Average | −1.2% | −2.7% | −2.4%
Average without F | −1.4% | −3.1% | −2.9%
Enc. Time | 100% | 100% | 100%
Dec. Time | 104% | 106% | 108%