## Slide 1: JCTVC-I0414
Oguz Bici, Kemal Ugur, Jani Lainema
Nokia
Removal of the restriction on the number of combined merge candidates

## Slide 2: Summary
Combined merge candidates introduced in HM4
  Maximum number to be tested for pruning process is limited to 5.
Pruning process removed in HM5
  Every valid combined candidate is directly inserted into the merge list
  Maximum combined candidates will never reach 5.
    Therefore, this limitation is obsolete.
Number of initial candidates | Maximum combined candidates to be added
1 | 0
2 | 2
3 | 2
4 | 1

## Slide 3: Summary
Proposed: Remove the limit in the text as a clean-up.
Results: No effect on bitstream
Text change: When combIdx is equal to ( numOrigMergeCand * ( numOrigMergeCand − 1 ) ) or numMergeCand is equal to MaxNumMergeCand or combCnt is equal to 5, combStop is set to TRUE.