## Slide 1
Chong Soon Lim
Sue Mon Thet Naing
Jizheng Xu
Bin Li
Panasonic Corporation
Microsoft Corporation
University of Science and Technology of China
JCTVC-I0420
<number>
JCTVC-I0420
Proposed fix on signaling of TMVP disabling flag
Notes: 22 March 2001
<number>

## Slide 2: Introduction
Current CD specifies the process to disable the TMVP is as follows: (JCTVC-G398)
  Signalling of enable_temporal_mvp_flag in PPS
  If (enable_temporal_mvp_flag==0 && temporal_id==0)
    Marking process of reference pictures in the DPB
    All pictures in the DPB are marked as “unused for temporal motion vector prediction”
  If enable_temporal_mvp_flag=0 or colPic is marked as “unused for temporal motion vector prediction”
    TMVP is not used as a candidate for inter prediction
JCTVC-I0420
<number>
Notes: 22 March 2001
<number>

## Slide 3: Problem Statements 1
  Marking process description specified in CD becomes ambiguous when signaling of temporal_id in all NAL unit headers (JCTVC-H0388) was adopted in 8th JCT-VC meeting.
    The classification of temporal_id is unclear and can be assumed that it is a PPS’s temporal_id
    The original intention for the marking process is to use the slice NAL’s temporal_id.
7.4.2.2 Picture parameter set RBSP semantics
enable_temporal_mvp_flag specifies whether temporal motion vector predictor can be used or not. If enable_temporal_mvp_flag is equal to 1, temporal motion vector predictors are used; otherwise (enable_temporal_mvp_flag is equal to 0), the temporal motion vector predictors are not used. enable_temporal_mvp_flag equal to 0 together with temporal_id equal to 0 also indicates that the marking process will occur before decoding the first picture with an output order greater than the current non-TMVP picture.
JCTVC-I0420
<number>
Notes: 22 March 2001
<number>

## Slide 4: Problem Statements 2
  A slice/picture that triggers the marking process can be lost or contains errors.
    Decoder may not know that the marking operation should be done and the last non-TMVP picture should be updated.
    Therefore, a mismatch between encoder and decoder may occur because of this marking process.
JCTVC-I0420
<number>

## Slide 5: Proposed method
  I0420 proposes 3 changes in specification as follows:
  Removing the marking process of reference picture in DPB. (reference pictures being marked as “unused for temporal motion vector prediction”.)
  Explicit signaling of enable_temporal_mvp_flag in slice headers for every P & B slices. This flag is explicitly signaled per slice instead of relying on frame-by-frame update of a buffer state.
  Enabling the same “refresh point” functionality as current CD by defining an encoder constraint replacing the normative decoder operation for marking pictures.
    enable_temporal_mvp_flag equal to 0 together with temporal_id equal to 0 also indicate that any pictures that follow the current picture both in decoding order and output order shall not use temporal motion vector prediction from any picture that precedes the current picture either in decoding order or output order.
JCTVC-I0420
<number>
Notes: Put encoder constraint to ensure that it serves the same functionality and minize the error propogation
22 March 2001
<number>

## Slide 6: Experimental Results
JCTVC-I0420
<number>
  The 1st test case, signaling of “enable_temporal_mvp_flag” in slice headers is conducted and compared with HM-6.1. No BD-Rate increment is observed under common test condition.
  The 2nd test case, disabling TMVP at every “refresh point” B-picture when temporal_id=0 is tested.
    2nd test case offers the currently supported error robustness for TMVP process with the cost of 0.3% BD-Rate increased as compared to no TMVP disabling to all frames.
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.6% | 0.5% | 0.4% | 0.5% | 0.1% | 0.4%
Class B | 0.2% | 0.2% | 0.2% | 0.2% | 0.1% | 0.1%
Class C | 0.2% | 0.2% | 0.2% | 0.2% | 0.1% | 0.1%
Class D | 0.4% | 0.4% | 0.3% | 0.3% | 0.1% | 0.3%
Class E |  |  |  |  |  | 
Overall | 0.3% | 0.3% | 0.3% | 0.3% | 0.1% | 0.2%
 | 0.3% | 0.3% | 0.3% | 0.3% | 0.1% | 0.2%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Notes: 22 March 2001
<number>

## Slide 7: Conclusion
I0420 proposes to explicitly signal the enable_temporal_mvp_flag at every P and B slice header.
The benefit includes cleaner design for TMVP disabling process.
It is suggested that the JCT-VC consider this proposal in refining the design of TMVP disabling process.
JCTVC-I0420
<number>

## Slide 8
Thank You!
JCTVC-I0420
<number>