## Slide 1: QP determination by lambda value
Bin Li, Dong Zhang, Houqiang Li, Jizheng Xu
University of Science and Technology of China
Microsoft Corp.

## Slide 2: Outline
Tune QP-lambda function in HEVC
Apply this QP-lambda function to HEVC
1.4%~1.8% Y bit saving without increasing the encoding/decoding time
  Bit saving for U and V is larger
QP-fixed encoding

## Slide 3: QP-lambda function in HEVC

## Slide 4: Apply new QP-lambda function to HEVC
Method 1: keep original QP setting, and use new QP-lambda relationship to determine lambda
Method 2: keep original lambda setting, and use new QP-lambda relationship to determine QP

## Slide 5: QP and lambda impact on bit allocation
Lambda is not only determined by QP, but also refined according to coding structure
Lambda is more important on bit allocation
  114% (RA-Main) and 77% (LB-Main) bitrate variation vs. 3% (RA-Main) and 3% (LB-Main) bitrate variation
We choose method 2
Notes: We perform two encoding methods and then compare the bitrate.
The first test is keeping the original QP setting but applying the lambda of the first picture, which is equal to or smaller than the original lambda value of each picture, to all the pictures (referred as original-QP encoding). The second test is keeping the original lambda setting but applying the QP of the first picture, which is also equal to or smaller than the original QP value of each picture, to all the pictures (referred as original-lambda encoding).

## Slide 6: Retune QP-lambda function
QP for intra picture: 22, 25, 28, 31, 34, 37, 40
Lambda values used in the experiments
 | Lambda values |  |  |  |  |  |  |  |  |  | 
 | Random Access |  |  |  |  | Low Delay |  |  |  | IBBB (Flat QP) | 
QPi | I | L0 | L1 | L2 | L3 | I | L0 | L1 | L2 | I | B
22 | 3.7 | 5.6 | 11.3 | 15.4 | 40.3 | 4.9 | 7.3 | 14.8 | 20.2 | 5.7 | 5.9
25 | 7.5 | 11.2 | 28.3 | 38.0 | 97.9 | 9.8 | 14.7 | 37.0 | 49.7 | 11.5 | 11.7
28 | 14.9 | 22.5 | 67.9 | 90.3 | 230.3 | 19.5 | 29.4 | 88.8 | 118.1 | 23.0 | 23.5
31 | 29.9 | 44.9 | 158.4 | 209.1 | 529.6 | 39.1 | 58.7 | 207.2 | 273.4 | 46.0 | 47.0
34 | 59.8 | 89.8 | 362.1 | 456.2 | 1105.3 | 78.1 | 117.4 | 473.5 | 596.6 | 91.9 | 94.0
37 | 119.5 | 179.6 | 724.2 | 912.4 | 2210.7 | 156.3 | 234.9 | 947.0 | 1193.1 | 183.8 | 187.9
40 | 239.0 | 359.2 | 1448.4 | 1824.8 | 4421.4 | 312.5 | 469.8 | 1894.0 | 2386.3 | 367.7 | 375.8

## Slide 7
Notes: QPi is the QP value of the intra picture.
The chroma distortion weight is kept unchanged

## Slide 8: QP setting
Original HM-6.0 QP setting
Refined QP setting
 | QP |  |  |  |  |  |  |  | 
 | Random Access |  |  |  |  | Low Delay B |  |  | 
QPi | I | L0 | L1 | L2 | L3 | I | L0 | L1 | L2
22 | 22 | 23 | 24 | 25 | 26 | 22 | 23 | 24 | 25
27 | 27 | 28 | 29 | 30 | 31 | 27 | 28 | 29 | 30
32 | 32 | 33 | 34 | 35 | 36 | 32 | 33 | 34 | 35
37 | 37 | 38 | 39 | 40 | 41 | 37 | 38 | 39 | 40
 | QP |  |  |  |  |  |  |  | 
 | Random Access |  |  |  |  | Low Delay B |  |  | 
QPi | I | L0 | L1 | L2 | L3 | I | L0 | L1 | L2
22 | 19 | 21 | 24 | 25 | 29 | 20 | 22 | 25 | 26
27 | 24 | 26 | 30 | 31 | 35 | 25 | 27 | 31 | 33
32 | 29 | 31 | 36 | 37 | 41 | 30 | 32 | 37 | 38
37 | 34 | 36 | 41 | 42 | 46 | 33 | 37 | 42 | 43

## Slide 9: Performance of retrained QP-lambda function
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −1.6% | −1.2% |  | 
Class B | −1.6% | −1.3% | −1.1% | −1.0%
Class C | −2.2% | −2.3% | −1.2% | −1.3%
Class D | −1.8% | −1.9% | −1.2% | −1.2%
Class E |  |  | −2.3% | −2.4%
Overall | −1.8% | −1.7% | −1.4% | −1.4%
Enc. Time | 100% | 100% | 100% | 100%
Dec. Time | 101% | 99% | 101% | 100%
The bit saving of U and V is a little larger, about 3%~4% on average
Original HM-6.0 is used as anchor in this table and all the following tables.

## Slide 10: LCU level multiple-QP optimization
3 QPs
5 QPs
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −1.1% | −0.8% |  | 
Class B | −1.1% | −0.9% | −0.5% | −0.4%
Class C | −1.3% | −1.3% | −0.7% | −0.7%
Class D | −1.1% | −1.1% | −0.7% | −0.7%
Class E |  |  | −1.0% | −1.1%
Overall | −1.2% | −1.1% | −0.7% | −0.7%
Enc. Time | 299% | 294% | 299% | 297%
Dec. Time | 102% | 101% | 102% | 101%
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −1.6% | −1.1% |  | 
Class B | −1.7% | −1.4% | −1.1% | −0.9%
Class C | −2.1% | −2.2% | −1.3% | −1.2%
Class D | −1.8% | −1.9% | −1.2% | −1.2%
Class E |  |  | −1.8% | −1.9%
Overall | −1.8% | −1.6% | −1.3% | −1.3%
Enc. Time | 497% | 486% | 498% | 494%
Dec. Time | 101% | 101% | 101% | 101%
Multiple-QP optimization does not work better than retuned QP-lambda relationship because of the QP search range is not large enough

## Slide 11: Multiple-QP optimization around QP determined by new function
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −2.0% | −1.4% |  | 
Class B | −2.2% | −1.8% | −1.7% | −1.4%
Class C | −2.8% | −2.8% | −1.8% | −1.8%
Class D | −2.3% | −2.3% | −1.6% | −1.7%
Class E |  |  | −2.6% | −2.4%
Overall | −2.3% | −2.1% | −1.9% | −1.8%
Enc. Time | 298% | 292% | 298% | 296%
Dec. Time | 101% | 100% | 102% | 101%
3 QPs optimization (around the QP determined by new relationship) works better than 5 QPs optimization (around original QP).

## Slide 12: Adaptive QP
Adaptive QP
New function + adaptive QP
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −1.4% | −1.3% |  | 
Class B | −1.0% | −0.7% | −2.0% | −1.7%
Class C | −1.4% | −0.9% | −2.0% | −1.6%
Class D | −0.9% | −0.5% | −1.4% | −1.1%
Class E |  |  | −1.4% | −1.1%
Overall | −1.1% | −0.8% | −1.8% | −1.4%
Enc. Time | 99% | 99% | 99% | 99%
Dec. Time | 101% | 99% | 101% | 100%
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | −1.6% | −1.3% |  | 
Class B | −1.9% | −1.6% | −2.0% | −1.8%
Class C | −3.0% | −2.9% | −2.3% | −2.2%
Class D | −2.4% | −2.2% | −1.9% | −1.6%
Class E |  |  | −3.4% | −3.5%
Overall | −2.2% | −2.0% | −2.3% | −2.2%
Enc. Time | 99% | 99% | 99% | 99%
Dec. Time | 100% | 99% | 101% | 100%
Adaptive QP was proposed in JCTVC-G382, non-normative part.
Proposed method can work well with adaptive QP.

## Slide 13: Conclusion
New QP-lambda function improves HEVC common test condition performance without increasing complexity
Easy to implement (about 10 lines code besides the lines reading and setting parameters)
Alternative method for multiple-QP optimization
Better start point for multiple-QP optimization
The current QP setting is not optimal when lambda has been modified manually