## Slide 1: I0487: On coefficient level remaining coding Wei-Jung Chien, Marta Karczewicz, Jianle Chen
Notes: Preparation for the 8-th JCT-VC meeting
Possible topics to look into (JS)

## Slide 2: Background
Binarization of coeff_abs_level_remaining in HM6.0
Decode Prefix0
Decode Prefix1
cRiceParam > 0
Yes
Is cTRMax reached
Yes
Decode Suffix (EG0)
End
No
No
Value | HM6.0 |  | 
 | Prefix0 | Prefix1 | Suffix
 | Truncated Rice |  | EG0
0 | 0 | 0 | 
1 | 0 | 1 | 
2 | 10 | 0 | 
3 | 10 | 1 | 
4 | 110 | 0 | 
5 | 110 | 1 | 
6 | 1110 | 0 | 
7 | 1110 | 1 | 
8 | 11110 | 0 | 
9 | 11110 | 1 | 
10 | 111110 | 0 | 
11 | 111110 | 1 | 
12 | 1111110 | 0 | 
13 | 1111110 | 1 | 
14 | 1111111 | 0 | 
15 | 1111111 | 1 | 0
16 | 1111111 | 1 | 100
17 | 1111111 | 1 | 101
18 | 1111111 | 1 | 11000
19 | 1111111 | 1 | 11001
20 | 1111111 | 1 | 11010
21 | 1111111 | 1 | 11011
22 | 1111111 | 1 | 1110000
23 | 1111111 | 1 | 1110001
… | … | … | …
cRiceParam = 1
May implemented as lookup table

## Slide 3: Proposed scheme
 | Prefix | Suffix (in bits)
0 ~ 1×2k-1 | 0 | k
1×2k ~ 2×2k -1 | 10 | k
2×2k ~ 3×2k -1 | 110 | k
3×2k ~ 4×2k -1 | 1110 | k
4×2k ~ 5×2k -1 | 11110 | k
5×2k ~ 6×2k -1 | 111110 | k
6×2k ~ 7×2k -1 | 1111110 | k
7×2k ~ 8×2k -1 | 11111110 | k
8×2k ~ 9×2k -1 | 111111110 | k
9×2k ~ 11×2k -1 | 1111111110 | k+1
11×2k ~ 15×2k -1 | 11111111110 | k+2
15×2k ~ 23×2k -1 | 111111111110 | k+3
… | … | 
Binarization of coeff_abs_level_remaining
  Similar to level coding table used in LCEC
  Suffix length depends only on the value of prefix
  No modification on parameter K update scheme (same as HM6.0)
  Flexible lookup table implementation for prefix

## Slide 4: Simulation Results
Test condition
  Common test condition
  Low QP test condition (12, 17, 22, 27)

## Slide 5: Conclusions
Binarization for coeff_abs_level_remaining
  Suffix length depends only on the value of prefix
  Simpler and flexible decoder design
  0.0% Y BD-rate change
Recommend adoption of the proposed binarization
Thanks to Panasonic (JCTVC-I0519) for cross-checking