## Slide 1: JCTVC-I0524: Hook for scalable extensions: video parameter set MPEG M24896: 3DV-HTM high-level syntax: video and sequence parameter set design
Miska M. Hannuksela, Dmytro Rusanovskyy Nokia Research Center

## Slide 2: Definitions
A component sequence can be for example a texture view, a depth view, or an enhancement layer of spatial/quality scalability.
  Bitstreams compliant with the current non-scalable HEVC design have only one component sequence.
An access unit consists of one or more component pictures.
  In the current HEVC specification a component picture is the coded picture of an access unit
  In the future scalable extensions it would be for example a view component, a depth map, or a layer representation.
JCTVC-I0524 / MPEG M24896
<number>

## Slide 3: Base Specification
Sequence parameter set (SPS)
Profile and level information removed
Slice header
The slice header of IDR and CRA pictures is proposed to include an identifier (ref_vps_id) of the active VPS of the coded video sequence.
video_parameter_set_rbsp( ) { | 
max_component_sequences_minus1 | u(5)
max_temporal_layers_minus1 | u(3)
for( i = 0; i <= max_component_sequences_minus1; i++ ) { | 
profile_struct( ) | 
for( j = 0; j < max_temporal_layers_minus1; j++ ) | 
level_idc[ i ][ j ] | u(8)
} | 
vps_id | ue(v)
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
Video parameter set (VPS)
Profile and level information for bitstream subsets defined for each component sequence.
Level information for temporal subsets of component sequences.
JCTVC-I0524 / MPEG M24896
<number>
Notes: <number>

## Slide 4: Scalable Extensions
NAL unit header:
reserved_one_5bits in the nal_unit syntax structure is re-specified to be called cpd_id_plus1, indicating an identifier for a component sequence/picture.
VPS is extended to contain:
  The dependencies between component sequences.
  The mapping of component sequence/picture identifiers to specific scalability properties (e.g. dependency_id, quality_id, view order index).
… | 
vps_extension1_flag | u(1)
if( vps_extension1_flag ) { | 
for( i = 1; i <= max_component_sequences_minus1; i++ ) { | 
num_ref_component_seq[ i ] | ue(v)
for( j = 0; j < num_ref_component_seq; j++ ) | 
ref_component_seq_id[ i ][ j ] | u(5)
} | 
num_component_seq_types | ue(v)
for( i = 1; i <= num_component_seq_types; i++ ) { | 
component_sequence_type[ i ] | ue(v)
component_sequence_property_len[ i ] | ue(v)
len[ i ] = component_sequence_property_len[ i ] | 
} | 
for( i = 1; i <= max_component_sequences_minus1; i++ ) { | 
component_sequence_type_idx[ i ] | ue(v)
tp = component_sequence_type_idx[ i ] | 
component_sequence_property[ i ] | u(len[tp])
} | 
} | 
JCTVC-I0524 / MPEG M24896
<number>
Notes: <number>

## Slide 5: 3D Scalable Extension
Mappings of the generic VPS extension to 3D:
The semantics of two values of component_sequence_type: texture view component, depth view component.
component_sequence_property_len = number of bits that covers the maximum number of views
component_sequence_property specifies the view order index within the component sequence
… | 
vps_extension1_flag | u(1)
if( vps_extension1_flag ) { | 
for( i = 1; i <= max_component_sequences_minus1; i++ ) { | 
num_ref_component_seq[ i ] | ue(v)
for( j = 0; j < num_ref_component_seq; j++ ) | 
ref_component_seq_id[ i ][ j ] | u(5)
} | 
num_component_seq_types | ue(v)
for( i = 1; i <= num_component_seq_types; i++ ) { | 
component_sequence_type[ i ] | ue(v)
component_sequence_property_len[ i ] | ue(v)
len[ i ] = component_sequence_property_len[ i ] | 
} | 
for( i = 1; i <= max_component_sequences_minus1; i++ ) { | 
component_sequence_type_idx[ i ] | ue(v)
tp = component_sequence_type_idx[ i ] | 
component_sequence_property[ i ] | u(len[tp])
} | 
} | 
JCTVC-I0524 / MPEG M24896
<number>