## Slide 1: Deblocking filter length adjustment
JCTVC-I0542
Andrey Norkin, Rickard Sjöberg
Ericsson
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 2: Deblocking decisions
dp0 = | p2,0 − 2*p1,0 + p0,0 | dq0 = | q2,0 − 2*q1,0 + q0,0 |
dp3 = | p2,3 − 2*p1,3 + p0,3 | dq0 = | q2,3 − 2*q1,3 + q0,3 |
        dpq0 = dp0 + dq0
dpq3 = dp3 + dq3
dp = dp0 + dp3 dq = dq0 + dq3
d = dp0 + dp3 + dq0 + dq3

## Slide 3: Deblocking decisions
Deblocking of the boundary:
d<β( QP)
Strong/weak filtering decisions:
2*dpqi < (β>>2)
and (|p3i - p0i| + |q0i – q3i|) < (β>>3)
and |p0i – q0i| < ((5*tC + 1)>>1)
Weak filter: one or two pixels from block boundary
dp < ( β + ( β >> 1 ) ) >> 3

## Slide 4: Three thresholds depending on β that control weak/strong filtering decisions
One or two pixels in weak filter:
    (3*β ) >> 4
Strong filter (3 pixels) or weak filter (1 or 2 pixels):
    β >> 3
    β >> 4
In order to adjust ”length” of deblocking filters, significant modification of β by sending beta_offset_div2 is needed

## Slide 5: Proposed to change
    Use in expressions
    (β+ (β>>2) ) >> 3
    β >> 3
    β >> 2
another beta value, called BetaLength
      BetaLength = β * (4 + LoopFilterLengthOffset),
where LoopFilterLengthOffset is signaled in slice header or APS
Thresholds become
    (BetaLength + (BetaLength>>2) ) >> 5
    BetaLength >> 5
    BetaLength >> 4

## Slide 6: Change of deblocking thresholds when sending LoopFilterLengthOffset = 1
Solid lines: initial Thresholds
Dashed lines: LoopFilterLengthOffset = 1

## Slide 7: Change of deblocking thresholds when sending LoopFilterLengthOffset = 2
Solid lines: initial Thresholds
Dashed lines: LoopFilterLengthOffset = 1

## Slide 8: Proposed syntax (slice header)

## Slide 9: Conclusions
It is proposed to signal deblocking_filter_length_offset in APS or slice header
Offset is used to ”relax” or ”restrict” conditions for application of longer deblocking filters
deblocking_filter_length_offset adjusts deblocking filter strength without modifying the number of edges to which deblocking is applied
Can be used together with beta_offset_div2 and tc_offset_div_2 in order to achieve even stronger deblocking filtering
It is proposed to include deblocking_filter_length_offset and proposed modifications to DIS text and next version of HM

## Slide 10
Notes: 2010-10-07
Ericsson AB 2010
<number>