## Slide 1
<number>
Unified context derivation with CABAC context reduction for last position coding
JCTVC-0574
Feng Zou, Oscar C. Au, Jingjing Dai, Xingyu Zhang, Chao Pang
HKUST

## Slide 2: JCTVC I0574 Outline
<number>
Context modeling for last significant coefficient position coding
Unified context derivation with CABAC context reduction for last position coding
Simulation Results
Notes: <number>

## Slide 3: JCTVC I0574 Related techniques
<number>
In HM6.0, last significant (none zero) coefficient position coding, comprises horizontal position x and vertical position y.
The last significant coefficient position is represented by a binary string which consists of two parts. The first part is truncated unary code where each bin is encoded with CABAC contexts, while the second part is fixed binary code with by-pass coding (no context).
Notes: <number>

## Slide 4: JCTVC I0574 Related Technique
<number>
Table 1. Last position coding for TU 4x4 Luma
Table 2. Last position coding for TU 8x8 Luma
Notes: <number>

## Slide 5: JCTVC I0574 Related Technique
<number>
Table 3. Last position coding for TU 16x16 Luma
Table 4. Last position coding for TU 32x32 Luma
Notes: <number>

## Slide 6: JCTVC I0574 Related Technique
<number>
Table 5. The context assignment for each bin in the truncated unary codeword for Luma.
Notes: <number>

## Slide 7: JCTVC I0574 Proposed Technique
<number>
Unified context derivation with CABAC context reduction for last position coding
Similar statistics for several bins for TU32x32, and therefore, several bins share the same CABAC contexts (Reducing the CABAC context from 15 to 13 for each direction x /y).
Table 7. The CABAC context index for each bin of different TU sizes(Total contexts 13 for each direction x/y)
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 3 | 4 | 4 | 5 |  |  |  | 
TU 16x16 | 6 | 6 | 7 | 7 | 8 | 8 | 9 |  | 
TU 32x32 | 10 | 10 | 10 | 10 | 11 | 11 | 11 | 11 | 12
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 3 | 4 | 4 | 5 |  |  |  | 
TU 16x16 | 6 | 6 | 7 | 7 | 8 | 8 | 9 |  | 
TU 32x32 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14
Table 8. The CABAC context index for each bin of different TU sizes (15 context for each direction x/y) in JCTVC-I0331
Notes: <number>

## Slide 8: JCTVC-I0574 Test Condition and Results
Test Condition and Results
The anchor is HM6.0 with encoding conditions specified in the common test conditions in JCTVC-H1100. .
Simulation results show that there is negligible loss under the common test condition
For last_significant_coeff_x_prefix, ctxIdxInc is derived as follows.
ctxIdxInc = m+ (binIdx>>n)
For last_significant_coeff_y_prefix, ctxIdxInc is derived as follows.
ctxIdxInc = m+ (binIdx>>n)
where m = 3* k + ((k+1)>>2) (1)
n = (k+1)>>1, ( different from n = (k+3)>>2 in I0331)
k= log2(TrafoWidth)-2 for last_significant_coeff_x_prefix, or
k= log2(TrafoHeight)-2 for last_significant_coeff_y_prefix.

## Slide 9: JCTVC-I0574 Conclusion
Reduce the CABAC contexts for significant coefficient position coding (3026, 13.3%) with no significant RD loss
Recommend to adopt them into the HEVC standard