## Slide 1: Performance evaluation of DST in intra prediction
JCTVC-I0582
K. Ugur, O. Bici

## Slide 2: Introduction Current HEVC CD:
For 4x4 Intra TU’s residual could be transformed:
  DCT for both horizontal and vertical transform
  DCT for horizontal and DST for vertical transform
  DST for horizontal and DCT for vertical transform
  DST for both horizontal and vertical transform
The horizontal and vertical transforms are adapted based on the intra prediction mode.
This proposal tests two simplifications:
Simplification 1: Use DST for all prediction modes for 4x4 intra
0.1% loss on average in All-Intra
Simplification 2: Use DST for all prediction modes except DC mode
No coding efficiency change

## Slide 3: Benefits
Both simplification has the following benefits:
No DCT-DST or DST-DCT (reduces number of transforms)
Transform does not depend on prediction direction
  In Simplification-2, it only depends if mode is DC or not
Text simplification
Decoder complexity reduction
  Less control logic in hardware
4x4 intra quant matrices could now be default for DST.
  See I0592 for a proposal
  Reduces the current subjective quality problem in HEVC

## Slide 4: Results
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.3% | -0.2% | -0.1% | -0.3% | -0.3%
Class B | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | -0.2%
Class C | 0.2% | -0.2% | -0.2% | 0.2% | -0.2% | -0.1%
Class D | 0.2% | -0.1% | -0.2% | 0.3% | -0.1% | -0.1%
Class E | 0.0% | -0.2% | -0.2% | 0.0% | -0.3% | -0.2%
Overall | 0.1% | -0.2% | -0.2% | 0.1% | -0.2% | -0.2%
 | 0.1% | -0.2% | -0.2% | 0.1% | -0.2% | -0.2%
Class F | 0.5% | 0.2% | 0.1% | 0.5% | 0.1% | 0.1%
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Class C | 0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class D | 0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class E | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
Overall | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Class F | 0.3% | 0.2% | 0.1% | 0.3% | 0.1% | 0.1%
Simplification-1
DST for all prediction modes
Simplification-2
DST for all prediction modes
DCT for DC mode

## Slide 5: Additional Results RDOQ-off
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Class C | 0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class D | 0.1% | -0.1% | -0.1% | 0.2% | -0.1% | -0.1%
Class E | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
Overall | 0.0% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class F | 0.3% | 0.2% | 0.2% | 0.3% | 0.1% | 0.4%
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
Class B | 0.0% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class C | 0.2% | -0.1% | -0.2% | 0.3% | -0.1% | -0.1%
Class D | 0.3% | -0.1% | -0.1% | 0.3% | -0.1% | -0.1%
Class E | 0.0% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Overall | 0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
 | 0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
Class F | 0.6% | 0.3% | 0.2% | 0.6% | 0.1% | 0.7%
Simplification-1
DST for all prediction modes
Simplification-2
DST for all prediction modes
DCT for DC mode

## Slide 6: Additional Results Low QP 2,7,12,17
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class D | 0.2% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class E | 0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Overall | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class F | 0.5% | 0.1% | 0.1% | 0.6% | 0.2% | 0.1%
Simplification-1
DST for all prediction modes
Simplification-2
DST for all prediction modes
DCT for DC mode
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class B | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class D | 0.2% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0%
Class E | 0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Overall | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class F | 0.8% | 0.2% | 0.2% | 0.7% | 0.2% | 0.2%