## Slide 1: DST quantization matrix for DST in intra prediction (JCTVC-I0592)
Jian Lou, Yue Yu, Vivian Kung,
Krit Panusopone, Limin Wang Motorola Mobility, Inc.
Notes: <number>

## Slide 2: Introduction
JCTVC-I0268 proposes 3 additional Q matrix to support mode dependent transform (DST/DCT, DCT/DST, DST/DST)
Concerns raised about Q matrix switching at 4x4 TU level
Switching problem also happens in mode dependent transform for intra 4x4 luma TU
JCTVC-I0582 proposes using 2D-DST for all intra 4x4 luma prediction modes

## Slide 3: Suggested Modifications
Two modifications based on JCTVC-I0582; 2D-DST used for intra 4x4 luma TU instead of combination of DST/DCT
First modification uses DST based Q matrix instead of current DCT based Q matrix for intra 4x4 luma TU
Second modification uses 2D-DST for intra 4x4 chroma TU in addition to intra 4x4 luma TU

## Slide 4: First modification (DST Q matrix)
DST based Q matrix is used for intra 4x4 luma TU
  (same as in JCTVC-I0268)
5 | 7 | 8 | 10
7 | 12 | 15 | 17
8 | 15 | 29 | 43
10 | 17 | 43 | 87

## Slide 5: Simulation results (Part 1) JCTVC-I0582 with DCT Q matrix

## Slide 6: Simulation results (Part 1) JCTVC-I0582 with DST Q matrix

## Slide 7: Simulation results (Part 1) JCTVC-I0582 with DCT Q matrix

## Slide 8: Simulation results (Part 1) JCTVC-I0582 with DST Q matrix

## Slide 9: Second modification (DST for chroma)
Use 2D-DST for intra 4x4 chroma TU
Harmonize transform operation with intra 4x4 luma TU; one transform for all intra 4x4 TU
Simplify operation by removing transform matrix switching under 8x8 TU

## Slide 10: Simulation results (Part 2)
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | 1.5% | 2.1% | 0.0% | 1.4% | 2.3%
Class B | -0.1% | 1.5% | 1.7% | -0.1% | 1.7% | 2.2%
Class C | -0.3% | 1.3% | 1.6% | -0.3% | 1.9% | 2.4%
Class D | -0.2% | 1.6% | 1.6% | -0.3% | 1.9% | 2.0%
Class E | -0.2% | 2.4% | 1.3% | -0.3% | 3.2% | 1.7%
Overall | -0.2% | 1.6% | 1.6% | -0.2% | 2.0% | 2.1%
 | -0.2% | 1.6% | 1.6% | -0.2% | 2.0% | 2.1%
Class F | -0.2% | 1.2% | 1.0% | -0.2% | 1.6% | 1.7%

## Slide 11: Conclusions
Frequent switching problem partially solved by using 2D-DST for intra 4x4 luma TU (JCTVC-I0582)
Using 2D-DST for all intra 4x4 TU removes all transform matrix switching under 8x8 TU level
Using DST based Q matrix when 2D-DST is used improves subject quality

## Slide 12
Thank You!
Notes: <number>