## Slide 1
Performance Comparison of HM 6.0 with Existing Still Image Compression Schemes Using a Test Set of Popular Still Images
T. Nguyen, D. Marpe

## Slide 2: Performance Evaluation
Using a test set of 32 RGB and 2 grayscale images
4:2:0 YCrCb subsampling same as in JPEG
Bit rates of interest from 0.25 to 1.75 bpp
BD rate as performance measure
Relative to JPEG, JPEG 2000, JPEG XR, WebP, H.264/AVC (intra-only)

## Slide 3: RD plot ‘barbara’
Chart: bits per pixel
| 0.242034912109375 | 0.48529052734375 | 0.738372802734375 | 1.1995544433593801 | 1.7940673828125 | 2.1578369140625
HEVC | 30.5882 | 34.4039 | 37.0238 | 40.3811 | 43.5839 | 45.4437
H.264/AVC | 28.4417 | 32.6363 | 35.355 | 37.4488 | 38.8396 | 41.0252 | 41.8215 | 43.4833
JPEG 2000 | 28.3645 | 32.1692 | 34.8445 | 37.1545 | 38.9107 | 40.4918 | 41.8868 | 43.1015
JPEG XR | 26.857 | 30.8763 | 33.6575 | 35.9509 | 37.5316 | 39.1309 | 40.5383 | 41.623
WebP/VP8 | 26.0184 | 30.0081 | 33.079 | 35.2547 | 37.1462 | 38.5397 | 39.6559 | 41.474
JPEG | 25.8548 | 30.0836 | 32.871 | 35.2777 | 36.8283 | 38.463 | 40.1193 | 41.5866

## Slide 4: RD plot ‘lena’
Chart: bits per pixel
| 0.24884033203125 | 0.513275146484375 | 0.785064697265625 | 1.2479248046875 | 1.451904296875 | 1.8461608886718801 | 2.0434265136718799
HEVC | 35.6043 | 38.4574 | 40.1939 | 42.5583 | 43.5896 | 45.6794 | 46.7677
H.264/AVC | 34.25 | 37.7529 | 39.4188 | 40.7782 | 41.5947 | 43.491 | 44.4947 | 45.5723
JPEG 2000 | 34.0898 | 37.2463 | 38.9133 | 40.3101 | 41.5 | 42.7311 | 43.7205 | 44.7689
JPEG XR | 33.0753 | 36.4922 | 38.1444 | 39.534 | 40.5554 | 41.6209 | 42.717 | 44.1453
WebP/VP8 | 33.2444 | 36.5488 | 38.4637 | 39.7546 | 41.0384 | 42.3424 | 43.0065 | 44.2766
JPEG | 30.9115 | 35.0513 | 37.0941 | 38.6941 | 39.5846 | 40.7503 | 41.4853 | 43.4918

## Slide 5: Results
Anchor ↓ | HEVC | H.264/AVC | JPEG 2000 | JPEG XR | WebP | JPEG
HEVC |  | 19.0 | 29.7 | 43.6 | 45.9 | 76.3
H.264/AVC | -15.8 |  | 9.3 | 20.5 | 21.6 | 48.1
JPEG 2000 | -22.6 | -8.2 |  | 10.2 | 11.4 | 35.6
JPEG XR | -30.0 | -16.8 | -9.6 |  | 0.7 | 23.4
WebP | -31.0 | -17.6 | -9.5 | -0.3 |  | 23.2
JPEG | -43.0 | -32.3 | -26.0 | -18.9 | -18.6 |