## Slide 1: An HEVC transcoder converting non-parallel bitstreams to/from WPP JCTVC-0032
Gordon Clare, Félix Henry – Orange Labs
Notes: presentation title
<number>

## Slide 2: Motivation
There is less and less control over content production
Non parallel-friendly bitstream produced by unaware devices/consumers will be made available in their compressed form only
There is need to convert a non parallel-friendly bitstream to a parallel friendly one
  This is possible only for parallel processing based on methods that do not break dependencies in the bitstream
We present a transcoder to/from WPP
Notes: presentation title
<number>

## Slide 3: Implementation
The transcoder consists of the following modification of the reference software
  In the HM7.0 decoder, the decoded symbols of the HM7.0 parser are passed to the HM7.0 entropy coder with appropriate WPP parametrization
    Note: the decoding process was not removed from the software, although it is not necessary for transcoding
  high level syntax (SPS, PPS, SH) is modified to take into account the addition/removal of related syntax elements:
    tiles_or_entropy_coding_sync_idc
    WPP substream entry points added or removed
  other high level syntax is simply passed through
Notes: presentation title
<number>

## Slide 4: Characteristics
Reversibility
  Bitstreams transcoded twice are bit-identical
Encoder
Transcoder
WPP off
WPP
Transcoder
Encoder
Transcoder
WPP
WPP on
Transcoder
WPP
identical
identical
Notes: presentation title
<number>

## Slide 5: Characteristics
Lossless transcoding (decoded sequence is not affected by transcoding)
Encoder
Transcoder
Decoder
WPP off
WPP
Decoder
Encoder
Transcoder
WPP
Decoder
WPP on
Decoder
identical
identical
Notes: presentation title
<number>

## Slide 6: Performance
Performance penalty of the bitstream obtained from transcoding
  Due to encoding choices made from different rate estimation than the final encoding
Encoder
Transcoder
WPP
WPP off
Encoder
WPP on
WPP
I: +0.1%
RA: +0.1%
LDB: +0.3%
Reference
Encoder
Transcoder
WPP
WPP on
Encoder
WPP off
I: +0.1%
RA: +0.2%
LDB: +0.3%
Reference
Notes: presentation title
<number>

## Slide 7: Runtime
Anchor: HM7.0 decoder (non-WPP bitstream)
  Parsing process + Decoding process
Measure: HM7.0 transcoding (Non-WPP to WPP)
  Parsing process + Decoding process(*) + Entropy encoding
 | AIMAIN | RAMAIN | LDBMAIN | LDPMAIN
Class A | 104% | 107% |  | 
Class B | 105% | 101% | 97% | 97%
Class C | 105% | 99% | 101% | 102%
Class D | 107% | 103% | 103% | 104%
Class E | 103% |  | 96% | 96%
Class F | 103% | 97% | 99% | 99%
Dec Time[%] | 105% | 102% | 99% | 99%
(*) This step is useless and takes most of the runtime
Notes: presentation title
<number>

## Slide 8: Conclusion
A transcoder to/from WPP is presented
The transcoder is reversible & lossless
  Reconstructed sequence is not affected by transcoding
The rate-distortion of a transcoded bitstream is very close to a «direct» bitstream
Main use case: add parallel friendliness to any bitstream
The software is provided to interested JTCVC experts
  on request to felix.henry@orange.com or gordon.clare@orange.com
Notes: presentation title
<number>

## Slide 9: Thank you
Notes: presentation title
<number>