## Slide 1: JCT-VC J0035 CE1: Nokia’s results on intra transform mode dependency simplifications
K. Ugur, O. Bici (Nokia)

## Slide 2: Introduction
For 4x4 Intra TU’s residual could be transformed:
  DCT for both horizontal and vertical transform
  DCT for horizontal and DST for vertical transform
  DST for horizontal and DCT for vertical transform
  DST for both horizontal and vertical transform
Horizontal and vertical transforms are adapted based on the intra prediction mode.
This contribution tests two simplifications:
Simplification 1 (Proposal): Use DST for all prediction modes for luma 4x4 intra TU’s
0.06% loss on average for All-Intra Main
Simplification 2: Use DST for all prediction modes except DC mode for luma 4x4 intra TU’s
0.01% loss on average for All-Intra Main

## Slide 3: Benefits
Both simplification has the following benefits:
No DCT-DST or DST-DCT (reduces number of transforms)
Transform does not depend on prediction direction
  In Simplification-2, it only depends if mode is DC or not
Text simplification
Decoder complexity reduction
  Less control logic in hardware

## Slide 4: Results Simplification 1
 | All Intra Main |  | 
 | Y | U | V
Class A | -0.1% | -0.1% | -0.2%
Class B | 0.0% | -0.2% | -0.2%
Class C | 0.2% | -0.2% | -0.2%
Class D | 0.2% | -0.1% | -0.2%
Class E | 0.0% | -0.2% | -0.2%
Overall | 0.1% | -0.2% | -0.2%
 | 0.1% | -0.2% | -0.2%
Class F | 0.5% | 0.1% | 0.1%
Enc Time | 99% |  | 
Dec Time | 100% |  | 
 | All Intra Main |  | 
 | Y | U | V
Class A | -0.1% | -0.2% | -0.1%
Class B | 0.0% | -0.2% | -0.2%
Class C | 0.1% | -0.2% | -0.2%
Class D | 0.2% | -0.1% | -0.1%
Class E | 0.0% | -0.1% | -0.2%
Overall | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.2% | -0.2%
Class F | 0.5% | 0.2% | 0.2%
Enc Time | 99% |  | 
Dec Time | 101% |  | 
 | All Intra Main |  | 
 | Y | U | V
Class A | 0.1% | -0.1% | -0.1%
Class B | 0.1% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.0%
Class D | 0.2% | 0.0% | 0.0%
Class E | 0.1% | -0.1% | -0.1%
Overall | 0.1% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0%
Class F | 0.8% | 0.1% | 0.1%
Enc Time | 99% |  | 
Dec Time | 100% |  | 
All Intra Main
All Intra Main Transform Skip Enabled
All Intra Main Low QP (2,7,12,17)

## Slide 5: Results Simplification 2
 | All Intra Main |  | 
 | Y | U | V
Class A | -0.1% | -0.1% | -0.1%
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.1% | -0.1% | -0.1%
Class D | 0.1% | 0.0% | -0.1%
Class E | 0.0% | -0.1% | -0.2%
Overall | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Class F | 0.3% | 0.1% | 0.1%
Enc Time | 101% |  | 
Dec Time | 99% |  | 
 | All Intra Main |  | 
 | Y | U | V
Class A | -0.1% | -0.1% | -0.1%
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | -0.1% | -0.1%
Class D | 0.1% | -0.1% | -0.1%
Class E | -0.1% | -0.1% | -0.2%
Overall | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Class F | 0.2% | 0.0% | 0.0%
Enc Time | 99% |  | 
Dec Time | 101% |  | 
 | All Intra Main |  | 
 | Y | U | V
Class A | 0.1% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.0%
Class D | 0.2% | 0.0% | 0.0%
Class E | 0.1% | -0.1% | -0.1%
Overall | 0.1% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0%
Class F | 0.5% | 0.1% | 0.1%
Enc Time | 99% |  | 
Dec Time | 100% |  | 
All Intra Main
All Intra Main Transform Skip Enabled
All Intra Main Low QP (2,7,12,17)

## Slide 6: Conclusion
We propose to use 2D DST for luma intra 4x4 TU’s regardless of the prediction mode.
Benefits
  No DCT-DST and DST-DCT adaptation
  Transform does not depend on prediction direction
  Simplification in the text
  Simplification in decoder complexity
This simplification comes with 0.06% coding efficiency drop in all-intra