## Slide 1: Encoder modification for SAO
E. Alshina, A. Alshin, J.H. Park
Samsung Electronics Ltd

## Slide 2: I0184: Encoder modification for SAO interleaving mode
I0184:
  Count hit-ratio of LCU with SAO off (hr_sao_off) at “depth_0”
  If hr_sao_off > 75% then SAO if off for Y&Cb&Cr for whole pictures with depth_1,2,3
Suggested:
  Count hr_sao_off_luma and hr_sao_off_chroma separately
  If hr_sao_off_Luma > 75% then SAO if off for Luma at higher depth
  If hr_sao_off_Chroma > 50% then SAO if off for Chroma at higher depth
depth_0
depth_1
depth_2
depth_3
7%
100%
0%
28%
32%
100%
71%
100%
42%
100%

## Slide 3: Test results
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.1% | -0.1% | 0.0% | -0.1% | 0.1%
Class B | -0.2% | 0.2% | 0.0% | -0.1% | 0.0% | -0.1%
Class C | -0.3% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1%
Class D | -0.5% | -0.3% | -0.3% | -0.4% | -0.3% | -0.4%
Overall | -0.3% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1%
Class F | -0.3% | -0.1% | 0.0% | -0.2% | -0.1% | -0.1%
Enc Time | 99% |  |  | 100% |  | 
Dec Time | 98% |  |  | 99% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class B | 0.0% | 0.3% | 0.1% | -0.1% | 0.1% | 0.4%
Class C | -0.1% | 0.0% | 0.2% | -0.1% | -0.1% | 0.0%
Class D | -0.3% | -0.3% | 0.0% | -0.2% | -0.4% | -0.3%
Class E | -0.1% | -0.2% | 0.0% | 0.0% | 0.0% | 0.3%
Overall | -0.1% | 0.0% | 0.1% | -0.1% | -0.1% | 0.1%
Class F | -0.3% | 0.2% | 0.4% | -0.1% | 0.5% | 1.0%
Enc Time | 100% |  |  | 100% |  | 
Dec Time | 99% |  |  | 102% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class B | -0.5% | 0.4% | 0.0% | -0.1% | 0.3% | 0.0%
Class C | -0.2% | -0.1% | 0.2% | -0.1% | -0.1% | 0.0%
Class D | -0.3% | 0.0% | 0.2% | -0.2% | 0.1% | -1.0%
Class E | -0.3% | -0.2% | 0.0% | -0.1% | 0.2% | -0.1%
Overall | -0.4% | 0.1% | 0.0% | -0.2% | 0.1% | -0.2%
Class F | -0.4% | 0.3% | -0.2% | -0.3% | 0.1% | -0.1%
Enc Time | 99% |  |  | 100% |  | 
Dec Time | 100% |  |  | 102% |  | 
Average BD-rate | Y | U | V
 | -0.2% | 0.0% | 0.0%

## Slide 4: Bins statistics
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI Main | 100.00% | 100.00% | 100.00% | 100.00%
RA Main | 97.91% | 99.99% | 47.01% | 98.03%
LB Main | 99.38% | 99.98% | 78.35% | 101.73%
LP Main | 99.15% | 99.82% | 78.54% | 100.70%
Average | 99.11% | 99.95% | 75.97% | 100.12%
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI HE10 | 100.00% | 100.00% | 100.00% | 100.00%
RA HE10 | 98.54% | 100.00% | 42.83% | 100.22%
LB HE10 | 99.74% | 99.99% | 84.21% | 102.51%
LP HE10 | 99.65% | 99.91% | 83.85% | 100.00%
Average | 99.48% | 99.98% | 77.72% | 100.00%
Statistically:
23% ctx coded bins reduction for SAO syntax
0.7% overall ctx coded bins reduction

## Slide 5: Conclusion
Based on reported results:
  0.2% Luma BD-rate gain without performance degradation for Chroma
  23% reduction of SAO ctx coded bins (0.7% of total amount ctx bins) reduction
Samsung recommends adoption of proposed
SAO search strategy modification for next
version of HM reference s/w.