## Slide 1: AhG6: On SAO type sharing between U and V components
E. Alshina, A. Alshin, J.H. Park
Samsung Electronics Ltd
G. Laroche, C. Gisquet, P. Onno
Canon Research Centre France

## Slide 2: Cb&Cr simultaneous processing
Interleaved Cr&Cb storage in memory allows to process Cr&Cb simultaneously
  In Intra prediction
    Cr&Cb share the same direction
  In MC
    Luma&Cr&Cb share MV
  In ALF
    Cr & Cb use the same filter shape
SAO type is allowed to be different for Luma, Cr and Cb (in HM7.0)
  SAO process for Chroma:
    De-interleaving
    SAO processing Cb
    SAO processing Cr
    Interleaving
Latency
Intra pred

## Slide 3: Smaller LCU sizes
LCU size | Y BD-rate,% | U BD-rate,% | V BD-rate,%
64x64 | -0.18% | 0.22% | 0.16%
32x32 | -0.21% | 0.05% | 0.00%
16x16 | -0.34% | -0.25% | -0.29%
Test:
SAO type
Merge left
Merge Up
shared between Cb&Cr

## Slide 4: Number ctx coded bins per sample
The worst case
  SAO magnitude
    1.45 bins/sample
Second worst case
  SAO type
    0.07 bins/sample 0.05 bins/sample

## Slide 5: Bins statistics
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI Main | 99.73% | 99.99% | 75.80% | 82.19%
RA Main | 98.39% | 99.99% | 59.76% | 92.72%
LB Main | 98.33% | 99.89% | 64.03% | 98.89%
LP Main | 98.22% | 99.81% | 65.87% | 96.77%
Average | 98.67% | 99.92% | 66.37% | 92.64%
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI HE10 | 74.21% | 83.99% | 74.21% | 83.99%
RA HE10 | 55.29% | 88.34% | 55.29% | 88.34%
LB HE10 | 59.00% | 96.28% | 59.00% | 96.28%
LP HE10 | 60.59% | 93.69% | 60.59% | 93.69%
Average | 62.27% | 90.58% | 62.27% | 90.58%
36% reduction of ctx coded bins in SAO
1.7% reduction of overall ctx coded bins

## Slide 6: Conclusion
Based on reported results:
36% reduction of SAO context coded bins (1.2% of total amount of context bins) reduction.
1 context model is removed from HEVC design.
0.2% average Luma BD-rate gain under HM7.0 conditions
Samsung and Canon recommend adoption of SAO type and merge flags sharing between U and V components to DIS text and next version of HM s/w.

## Slide 7: Small syntax changes

## Slide 9: Context reduction