## Slide 1: Modification 1
Modification 1
  the SAO type index is coded with a truncated unary code (cMax=5) instead of a unary code
  reduces the maximum number of context coded bins for each SAO type index syntax element by 1
  Average (Main/HE10 AL, RA, LB): 0.0%, -0.3%, -0.2%

## Slide 2: Truncated Unary - results
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.2%
Class B | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.3%
Class C | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.2%
Overall | 0.0% | -0.2% | -0.2% | 0.0% | -0.1% | -0.2%
 | 0.0% | -0.2% | -0.2% | 0.0% | -0.1% | -0.2%
Class F | 0.0% | -0.2% | -0.2% | 0.0% | -0.3% | -0.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.6% | -0.4% | 0.1% | -0.3% | -0.3%
Class B | 0.0% | -0.3% | -0.3% | 0.0% | -0.3% | -0.4%
Class C | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | -0.2%
Class D | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.2%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.3%
 | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.3%
Class F | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | -0.4%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 102% |  |  | 102% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.4% | -0.5% | 0.0% | -0.2% | -0.1%
Class C | -0.1% | -0.5% | -0.4% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.2% | 0.2% | 0.0% | -0.2% | -0.1%
Class E | -0.1% | -0.5% | -0.4% | 0.0% | -0.5% | -0.3%
Overall | -0.1% | -0.4% | -0.3% | 0.0% | -0.3% | -0.2%
 | -0.1% | -0.4% | -0.3% | 0.0% | -0.2% | -0.1%
Class F | -0.2% | -0.5% | -0.4% | 0.1% | -0.1% | 0.6%
Enc Time[%] | 101% |  |  | 102% |  | 
Dec Time[%] | 102% |  |  | 103% |  | 

## Slide 3: Modification 2
Modification 2
  first bin signaling SAO on/off is coded with the first context
  second bin signaling band/edge offset is coded with the second context
  If edge offset is used, the remaining bins signal the edge offset type which is coded with a fixed length code of 2 bins in bypass mode
  limits the number of context coded bins for each syntax element to 2 and the total number of bins to 4
  Average (Main/HE10 AL, RA, LB): 0.0%, -0.3%, -0.4%

## Slide 4: 2 bins + FLC - results
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | -0.2%
Class B | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.3%
Class C | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.1%
Class E | 0.1% | -0.4% | -0.6% | 0.0% | -0.2% | -0.3%
Overall | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.2%
Class F | 0.0% | -0.3% | -0.3% | 0.0% | -0.3% | -0.3%
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 102% |  |  | 101% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.6% | -0.5% | 0.0% | -0.3% | -0.2%
Class B | 0.0% | -0.3% | -0.4% | 0.0% | -0.3% | -0.4%
Class C | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.3%
Class D | 0.0% | -0.2% | -0.4% | 0.0% | -0.1% | -0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.3%
 | 0.0% | -0.4% | -0.4% | 0.0% | -0.2% | -0.3%
Class F | -0.1% | -0.3% | -0.4% | 0.0% | -0.2% | -0.4%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.5% | -0.5% | 0.0% | -0.2% | -0.6%
Class C | 0.0% | -0.4% | -0.6% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.3% | -0.2% | 0.0% | 0.0% | -0.3%
Class E | 0.0% | -0.6% | -1.2% | 0.1% | -0.6% | -0.2%
Overall | 0.0% | -0.4% | -0.6% | 0.0% | -0.2% | -0.4%
 | 0.0% | -0.4% | -0.6% | 0.0% | -0.2% | -0.3%
Class F | -0.2% | -0.8% | -0.6% | 0.0% | -0.5% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |