## Slide 1: J0066 Cross Slice Deblocking
Pieter Kapsenberg Intel Corp

## Slide 2: Problem Statement
HEVC In-loop filtering specifies all vertical edges are filtered prior to filtering horizontal edges.
This creates a dependency on previous slice data regarding the following slice header syntax elements:
  tc_offset_div2
  beta_offest_div2
Common conditions does not vary these per slice.

## Slide 3: Diagram
In this diagram, the red dashed lines indicate an LCU boundary
Edge 0 and 1 must be processed before 2 and 3 can be.
Edge 0 and 2 require tc_offset_div2 and beta_offset_div2 from potentially 2 previous slices

## Slide 4: Worst Case
In this diagram, the green line is a tile boundary, the squares indicate LCUs
Here potentially every left and upper neighboring LCU could belong to a different slice
Necessary to load a whole column of beta/tc parameters from disjointed previous slices
For 16x16 LCU in a 1080P picture, a slice could need data from as many as (68+119) previous slices.

## Slide 5: Proposed Solution
Mandate that tc_offset_div2 and beta_offset_div2 are identical for all slices in a picture.
Text edit (addition highlighted):
Possible issue with slice-level flexibility / adaptability

## Slide 6: Alternative Idea
Follow edge order 1, 4, 3, 5
  Not as easy to multi-thread
  More invasive text edit
  Algorithm change
    Likely minimal BD impact