## Slide 1: Motion vector prediction issue for long-term reference picture
JCTVC-J0071
Y. Takahashi, O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
10th Meeting: Stockholm, SE, 11–20 July 2012

## Slide 2: One Page Summary
Background
  Current CD supports two types of reference pictures, which are short-term reference picture (STRP) and long-term reference picture (LTRP).
  In general, a delta POC value between the target picture and LTRPs is much larger than the value between the target picture and STRPs.
Problem
  Since the correlation of MVs referring the different types of reference pictures is low, predicted motion vectors (PMV) are sub-optimal in some cases.
Proposal
  Mark PMV “unavailable” when the types of reference pictures for target MV and for PMV are different.
  Minimal changes for Ver.1 decoder as a hook for the 3D extension, in which LTRPs are used for inter-view prediction.
Notes: This is contents.

## Slide 3: On HEVC version 1
3
POC
STRP
LTRP
Current Pic.
Large delta POC
Small delta POC
reference picture for a target MV | reference picture for a PMV | PMV availability in the draft/HM7 | PMV availability in proposal
STRP | STRP | “available” | “available”
STRP | LTRP | “available” but not scaled | “unavailable”
LTRP | STRP | “available” but not scaled | “unavailable”
LTRP | LTRP | “available” but not scaled | “available” but not scaled
target MV
PMV

## Slide 4: On 3D extension
4
POC
STRP
LTRP
Current Pic.
reference picture for a target MV | reference picture for a PMV | PMV availability in the draft/HM7 | PMV availability in proposal
STRP (inter) | STRP(inter) | “available” | “available”
STRP (inter) | LTRP (inter-view) | “available” but not scaled | “unavailable”
LTRP (inter-view) | STRP (inter) | “available” but not scaled | “unavailable”
LTRP (inter-view) | LTRP (inter-view) | “available” but not scaled | “available” but not scaled
Inter-view
inter

## Slide 5: Remarks
We have provided the draft text for HEVC WD7 and the source code (patch) implemented on HM-7.1.
Our proposal is cross-checked by Samsung (JCTVC-J0356).