## Slide 1: AHG4: Enable parallel decoding with tiles
07/31/26
<number>
Minhua Zhou, Vivienne Sze
Texas Instruments Inc., USA
JVTVC-J0088

## Slide 2: Summary of proposal
07/31/26
<number>
Define companion “parallel” levels for level 5.2 and above
  Enable parallel decoding by mandating uniformed spaced tiles (or sub-pictures)
  To enable parallel decoding on multiple core platforms with pixel-rate balancing among cores
  To allow building a multi-core decoder by simply replicating the single core decoders without need of increasing the line buffer size
The current levels remain unchanged
  A decoder conforming to a level can decode “parallel” stream at same level
  No tiles or other parallel tools are mandated

## Slide 3: Why multi-core parallel decoding?
07/31/26
<number>
CABAC decoding is bottleneck for real-time decoding
Single core real-time decoding for UHD is only possible when the CABAC parsing can be decoupled, latency, area and power consumption are not a concern
  Level 6.2, 800 Mbits/sec => ~500 MHz assuming 2 bin/sec
However, for low-latency real-time applications MHz requirements are much higher, cannot be handled by single core
Level | Max LumaPR | Max bit rate MaxBR (kbits/s) | minCR | max bins per 16x16 | MHz (frame decoupling) -1 frame | MHz (LCU pipeline)
4 | 62,668,800 | 15,000 | 4 | 5272 | 137 | ??
4.1 | 62,668,800 | 30,000 | 4 | 5272 | 137 | 
4.2 | 133,693,440 | 30,000 | 4 | 5272 | 291 | 
4.3 | 133,693,440 | 50,000 | 4 | 5272 | 291 | 
5 | 267,386,880 | 50,000 | 6 | 5272 | 406 | 
5.1 | 267,386,880 | 100,000 | 8 | 5272 | 317 | 
5.2 | 534,773,760 | 150,000 | 8 | 5272 | 634 | 
6 | 1,002,700,800 | 300,000 | 8 | 5272 | 1189 | 
6.1 | 2,005,401,600 | 500,000 | 8 | 5272 | 2379 | 
6.2 | 4,010,803,200 | 800,000 | 6 | 5272 | 6094 | 

## Slide 4: Highlights of Proposal
07/31/26
<number>
Mandate sub-pictures for high levels. A picture is divided into a number of sub-pictures of equal size (in units of LCUs)
Sub-pictures are independent, only in-loop filters can be allowed to cross the sub-picture boundaries
Tiles, slices, entropy slices and WPP are contained in sub-pictures and cannot cross sub-picture boundaries
The sub-picture partitioning information is signaled with tile syntax, and realized by imposing constraints on tile partitioning
Sub-picture entries in bitstream are signaled in APS (see JCTVC-J0081)
Add companion “parallel” levels for level 5.2 and above

## Slide 5: Sub-picture Partitioning & Signaling (option 1)
A sub-picture is a uniformly spaced tile ( no syntax change is required)
  Encoder and decoder have the same degree of parallelism
  Number of mandated tiles can be derived from level_id
Tile 00
Tile 10
Tile 30
Tile 20
Sub-pic1
Sub-pic0
Sub-pic2
Sub-pic3
Sub-picture boundaries
column_width[0]
column_width[1]
row_height[0]
row_height[1]

## Slide 6: Number of Tiles Specification (option 1)
07/31/26
<number>
Level limits (assuming 4kx2k@30 single core decoder capability)

## Slide 7: Sub-picture Partitioning & Signaling (option 2)
07/31/26
<number>
Sub-picture partitioning and signaling is realized by imposing constraints on tiles. If sub-pictures are present,
  Tiles can be evenly or unevenly divided in both vertical and horizontal directions, but there must be num_subPic_rows -1 bottom tile row boundaries that are coincident with the horizontal sub-picture boundaries
  Tiles can be evenly or unevenly divided in horizontal direction, but there must be num_subPic_columns -1 right-hand tile column boundaries that are coincident with the vertical sub-picture boundaries
Tile 00
Tile 01
Tile 10
Tile 11
Tile 30
Tile 31
Tile 20
Tile 21
Sub-pic1
Sub-pic0
Sub-pic2
Sub-pic3
Sub-picture boundaries
column_width[0]
column_width[1]
column_width[2]
column_width[3]
row_height[0]
row_height[2]
Tile 02
Tile 03
Tile 12
Tile 13
Tile 22
Tile 23
Tile 32
Tile 33
Syntax change in PPS ()

## Slide 8: Number of Sub-pictures Specification (1)
07/31/26
<number>
Specify total number of sub-pictures and minimum number of sub-picture columns for each level, and constrain both number of sub-picture rows and columns to be power of 2
  Avoid needs of single core line buffer increase when replicating single cores to build up multi-core platforms
    e.g. single core capability is 4Kx2K@30, if the minimum number of sub-picture columns is specified as 2, then 8Kx4K@30 decoder can be built by replicating 4Kx2K@30 four times.
  Maintain flexibility of sub-picture partitioning
    e.g. a picture can be divided either in 2x2 or 4x1 sub-pictures)
  Facilitate pixel-rate balancing when number of decoder cores is unequal to number of sub-pictures in the bitstreams
    e.g. 4 sub-pictures in bitstream, 2 decoder cores, each core processes two sub-streams)

## Slide 9: Number of Sub-picture Specification (2)
07/31/26
<number>
Level limits (assuming 4kx2k@30 single core decoder capability)

## Slide 10: Conclusions
07/31/26
<number>
Single core decoder
(slices, ES WPP)
Single core decoder1
(slices, ES WPP)
Single core decoder2
(slices, ES WPP)
Single core decoder3
(slices, ES WPP)
Single core decoder4
(slices, ES WPP)
Sub-picture boundary processing core
up to e.g.4kx2K@30
up to e.g. 8Kx4K@30
It is recommended to add “parallel” levels to mandate sub-pictures (signaled with tile syntax) for level 5.2 and above to enable parallel decoding on multi-core platforms
The current level specification remains unchanged.