## Slide 1: JCTVC-J0091: Chroma QP Offsets and Chroma Deblocking Filter
Geert Van der Auwera, Marta Karczewicz

## Slide 2: Summary
The cb_qp_offset and cr_qp_offset syntax elements are signalled in the PPS and specify the offsets to the luma QP used for deriving the chroma QP values.
The HM7 chroma deblocking filter derives the chroma filtering strength without taking into account the cb_qp_offset and cr_qp_offset values, which can significantly change the chroma QP values for coding and, therefore, the filtering strength of chroma blocking artifact edges can be too weak or too strong.
It is proposed to include the cb_qp_offset and cr_qp_offset values into the chroma deblocking filtering process.

## Slide 3: Chroma QP Offset and Deblocking
CD Text:
  “cb_qp_offset, cr_qp_offset are specifying the offset to the luma quantization parameter QP’Y used for deriving QP’Cb and QP’Cr , respectively”
Deblocking filter typically looks up the tC parameter in a table based on the QPC value that is derived as follows:
  QPC = QpUV ( (QPY,P + QPY,Q + 1)/2 )
Problem is that the chroma QP offset values, cb_qp_offset and cr_qp_offset, are not considered and since the range of these offset values is significant (-12 … 12), the deblocking filter may apply a deblocking strength to the chrominance components that is either too weak or too strong, which results in reduced chroma fidelity.

## Slide 4: Chroma QP Offset and Deblocking
Proposed to include the cr_qp_offset and cb_qp_offset values in the computation of the QPC values that are used to look up tC parameters for deblocking filtering the Cb and Cr components, as follows:
    QPCr = QpUV ( (QPY,P + QPY,Q + 1)/2 + cr_qp_offset )
    QPCb = QpUV ( (QPY,P + QPY,Q + 1)/2 + cb_qp_offset )
Separate tC values for Cb and Cr are looked up in a table based on the computed QPCr and QPCb (constant 2 is added for Bs=2)
Under common test conditions, the HM7.0 anchor is reproduced

## Slide 5: Chroma QP Offset and Deblocking
Deblocking without chroma QP offset (QP=27; cr/cb_qp_offset=12)

## Slide 6: Chroma QP Offset and Deblocking
Deblocking & chroma QP offset (QP=27; cr/cb_qp_offset=12)

## Slide 7: Chroma QP Offset and Deblocking
Deblocking without chroma QP offset (QP=27; cr/cb_qp_offset=12)

## Slide 8: Chroma QP Offset and Deblocking
Deblocking & chroma QP offset (QP=27; cr/cb_qp_offset=12)

## Slide 9: Conclusion
Proposed to include the cr_qp_offset and cb_qp_offset syntax element (PPS) values into the derivation of the QPC values that are used to configure the chroma deblocking filtering strength
This way too weak or too strong chroma filtering is avoided in case cr_qp_offset or cb_qp_offset are nonzero.