## Slide 1: JCTVC-J0137 AHG9: New High-level Syntax for Simple HEVC stream editing
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
10th JCT-VC meeting, Stockholm, SE, 11-20 July 2012

## Slide 2: Summary
Purpose
  Simple HEVC bitstream editing
Proposed enhancements
  Alternatives of cpb_removal_delay and dpb_output_delay for TFD picture removal
  New SEI indicating editing point
  New parameter indicating continuity of bitstream at BLA picture
Draft text is ready

## Slide 3: Background Simple HEVC bitstream editing

## Slide 4: Requirement on simple bitstream editing
HEVC Bitstream BSA
HEVC Bitstream BSB
Same size/rate
CRA
BLA
HEVC Bitstream BSA+B
Conformance
HRD continuity (decode + output)
Required operation
No need for decoding + re-encoding
Minimum modification on bitstream, preferably only at CRA picture
Introduction of BLA picture resolves the issue of discontinuous POC at editing point, but there remains other issues.
Concatenation
+ header manipulation

## Slide 5: Proposal 1 Alternatives of cpb_removal_delay and dpb_output_delay for TFD picture removal

## Slide 6: Discontinuity in TFD picture removal
Bitstream BSA
I68
B66
B65
B67
I72
B70
B69
B71
P76
B74
B73
B75
BPSEI
CRA
TFD
TFD
TFD
Decode/output delay
cpb_removal_delay
4
1
2
3
4
5
6
7
dpb_output_delay
5
2
0
1
5
2
0
1
cpb_removal_delay
dpb_output_delay
3
4
0
1
1
2
5
2
N/A
2
Display order
I68
B65
B66
B67
B69
B70
B71
B73
B74
B75
P76
I72
B70
B69
B71
P76
B74
B73
B75
I72
P76
B74
B73
B75
BPSEI
Sub-bitstream BSB
I72
P76
B74
B73
B75
BPSEI
CRA
B73
B74
B75
P76
I72
Display order
I72
Decoding from I72
with TFD picture removal
Picture
7
1
Correct
decode/output delay
Burden to decoder
Decremented by
#TFD pictures
Set to sps_num_reorder_pics

## Slide 7: Proposal
Alternatives of cpb_removal_time and dpb_output_timing
Similar to alt_initial_cpb_removal_delay(_offset)
buffering_period( payloadSize ) { | Descriptor
seq_parameter_set_id | ue(v)
if( !sub_pic_cpb_params_present_flag ) | 
rap_cpb_params_present_flag | u(1)
.... | 
initial_alt_cpb_removal_delay[ SchedSelIdx ] | u(v)
initial_alt_cpb_removal_delay_offset[ SchedSelIdx ] | u(v)
.... | 
if ( rap_cpb_params_present_flag ) { | 
alt_cpb_removal_delay_offset | ue(v)
alt_dpb_output_delay | u(v)
} | 
} | 
At decoder
If TFD pictures following BLA picture are regarded as removed (i.e. nal_unit_type of BLA picture is 7, and rap_cpb_params_present_flag = 1)
cpb_removal_delay of pictures following BLA picture is decremented by alt_cpb_removal_delay_offset
dpb_removal_delay of BLA picture is set to alt_dpb_output_delay

## Slide 8: Proposal 2 New SEI indicating editing point

## Slide 9: Discontinuity of display before editing point
TIME
Bitstream A
I12
B10
BPSEI
B9
B11
P16
B14
B13
B15
Bitstream B
Editing point
I68
B66
B65
B67
I72
B70
B69
B71
P76
B74
B73
B75
BPSEI
BPSEI
CRA
TFD
TFD
TFD
Bitstream
A + B
I12
B10
BPSEI
B9
B11
P16
B14
B13
I72
BPSEI
BLA
P76
B74
B73
B75
Display order
I12
B9
B10
B11
B13
B14
B15
Display order
I68
B65
B66
B67
B69
B70
B71
I72
B73
B74
B75
P76
Display order
B9
B10
B11
I12
B13
B14
P16
I72
B73
B74
B75
P76
Editor shall
detect the right editing point (B11 or B15), or
change dpb_output_delay of B16
Not allowed if fixed_pic_rate_flag is 1
Burden to editor

## Slide 10: Proposal
EPSEI: New SEI indicating editing point
editing_point( payloadSize ) { | Descriptor
if( NalHrBpPresentFlag ¦¦ VclHrdBpPresentFlag ) | 
cpb_status_present_flag | u(1)
if( cpb_status_present_flag ) { | 
if( NalHrdBpPresentFlag ) { | 
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
cpb_offset[ SchedSelIdx ] | u(v)
} | 
} | 
if( VclHrdBpPresentFlag ) { | 
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
cpb_offset[ SchedSelIdx ] | u(v)
} | 
} | 
} | 
} | 
EPSEI indicates the “right” editing point to editor
cpb_offset specifies SchedSelIdx-th CBP fullness when picture with EPSEI is decoded.

## Slide 11: Proposal 3 New parameter indicating continuity of bitstream at BLA picture

## Slide 12: cpb_removal_delay of BLA picture (1/2)
Requirements on cpb_removal_delay of BLA picture
for continuous HRD operation (both CPB and DPB) at editing point
1) Shall be larger than that of preceding picture
I12
B10
BPSEI
B9
B11
P16
B14
B13
I72
BPSEI
BLA
cpb_removal_delay
7
8
2) Shall reflect sps_num_reorder_pics of two bitstreams
P76
B74
B73
B75
I12
B10
BPSEI
B9
B11
P16
B14
B13
I72
BPSEI
BLA
P76
B73
B74
B75
Display order/timing
B9
B10
B11
I12
B13
B14
P16
I72
B73
B74
B75
P76
Decoding time
B15
I12
B10
B9
B11
P16
B14
B13
B15
I72
P76
B73
B74
B75
9
BPSEI
B15
B15
sps_num_reorder_pic = 1
sps_num_reorder_pic = 2
3) Shall not occurs CPB underflow/overflow
→ next page

## Slide 13: cpb_removal_delay of BLA picture (2/2)
TIME
CPB fullness
TIME
CPB fullness
iCRD(A)
iCRD(B)
iCRD(B)
Underflow
TIME
CPB fullness
2*tc
cpb_position @EPSEI
tr,n(0)
tr,n(1)
tr,n(2)
EPSEI
tr,n(0)
tr,n(0)
tr,n(1)
tr,n(2)
tr,n(3)
tc
tr,n(0)
tr,n(1)
tr,n(2)
tr,n(3)
Bitstream A
Bitstream B
iCRD: initial_cpb_removal_delay / 90000
Bitstream A+B
Bitstream A+B
Delay resolves underflow

## Slide 14: Problem
Decoder is not sure whether proper cpb_removal_delay is set at BLA picture.
→ Decoder would reset decoding/output process, then discontinuity occurs
TIME
CPB fullness
iCRD(A)
iCRD(B)
tr,n(0)
tr,n(1)
tr,n(2)
tr,n(3)
tc
Bitstream A
Bitstream B
Decoder resets decoding process, and restarts after iCRD(B)

## Slide 15: Proposal
One flag indicates continuity at BLA picture
buffering_period( payloadSize ) { | Descriptor
seq_parameter_set_id | ue(v)
} | 
if(NalHrdBpPresentFlag ¦¦ VclHrdBpPresentFlag ) | 
continuous_hrd_flag | u(1)
} | 
continuous_hrd_flag makes sense only at BLA picture.
If continuous_hrd_flag is 1, all of the following conditions are satisfied.
Same picture size, same picture rate before and after BLA picture
No CPB underflow or overflow occurs
DPB output times of all pictures satisfy constraint with fixed_pic_rate_flag = 1
  The value of to,dpb( n ) in Equation C-13 is always equal to tc when fixed_pic_rate_flag is equal to 1.