## Slide 1: JCTVC-J0139: AhG6 SAO Parameter Estimation Using Non-deblocked Pixels
<number>
Woo-Shik Kim
Texas Instruments Inc., USA
Notes: <number>

## Slide 2: LCU Based SAO Parameter Estimation
<number>
HM-7.0 supports LCU based SAO parameter estimation
  Advantages: local adaptation, low-delay processing
SAO is applied after deblock filtering
Red pixels are not used for SAO parameter estimation in HM-7.0 for low-delay processing as they are not deblock filtered yet
Blue pixels are not used, too, due to edge offset
 | C |  |  |  | C |  |  |  | C |  |  |  | C | 
LCU
One line delay due to EO
Non-deblock-filtered
pixels
< EO filter window shapes >
Notes: <number>

## Slide 3: Low-delay Processing in HM-7.0
<number>
Total 4 bottom lines and 5 right column lines for Y and 2 bottom/3 right lines for Cb/Cr are not used for SAO parameter estimation in HM-7.0
Occupancy ratio of removed pixels for SAO parameter estimation according to LCU sizes in HM-7.0
SAO performance is dropped due to inaccurate estimation
LCU size | number of pixels in LCU | number of removed pixels in LCU | occupancy ratio of removed pixels (%)
1616 | 256 | 124 | 48.4
3232 | 1024 | 268 | 26.2
6464 | 4096 | 556 | 13.6
48% for Y, 81% for Cb/Cr in case of 16x16 LCU
14% for Y, 26% for Cb/Cr in case of 64x64 LCU
Notes: <number>

## Slide 4: Proposed Methods
<number>
Non-normative proposal to improve SAO parameter estimation accuracy at the encoder side with low-delay processing
Accurate number of unavailable pixel lines depending on SAO type
Use of non-deblocked pixels instead of removing unavailable pixels for low-delay processing
sao_type_idx | Luma |  | Chroma | 
 | bottom lines | right column lines | bottom lines | right column lines
0 | N/A | N/A | N/A | N/A
1 | 3 | 5 | 1 | 3
2 | 4 | 4 | 2 | 2
3 | 4 | 5 | 2 | 3
4 | 4 | 5 | 2 | 3
5 | 3 | 4 | 1 | 2
Notes: <number>

## Slide 5: Experimental Results
<number>
(%)
Anchor is HM-7.0
 | LCU size | average excluding class F |  |  | average of class F |  | 
 |  | Y | Cb | Cr | Y | Cb | Cr
Low-delay B Main | 16 | -0.3% | 0.1% | -0.3% | -1.5% | -0.8% | -0.4%
 | 32 | -0.3% | -0.9% | -1.1% | -0.9% | -1.3% | -3.1%
 | 64 | -0.1% | -0.9% | -1.3% | -0.3% | -1.2% | -1.2%
Low-delay P Main | 16 | -1.8% | -0.4% | -0.4% | -1.8% | -1.8% | -1.7%
 | 32 | -0.9% | -1.5% | -1.5% | -0.9% | -1.5% | -1.5%
 | 64 | -0.3% | -1.2% | -1.2% | -0.4% | -1.6% | -1.4%
Notes: <number>

## Slide 6: Conclusions
<number>
Non-normative proposal to improve SAO encoding in interleaving mode
SAO parameter estimation using non-deblocked pixels for unavailable area for low-delay processing
Coding efficiency improvements by 1.8% in case of LCU size 16x16 and 0.3% in case of LCU size 64x64 in Low-delay P Main
Recommend to adopt in HM-7.0
Notes: <number>