## Slide 1: JCTVC-J0140: AhG6 SAO Complexity Reduction with SAO LCU Flag Coding
<number>
Woo-Shik Kim, Do-Kyoung Kwon
Texas Instruments Inc., USA
Notes: <number>

## Slide 2: SAO Parameter Signaling in HM-7.0
<number>
Slice level
  SAO enable flag for luma, and flags for chroma when luma flag is on
LCU level for each color component
  Merge left flag
  Merge up flag
  SAO type when merge is not used
  EO: 4 offset values, BO: band position + 4 offset values
sao_type_idx | SAO type
0 | Not applied
1 | 1D 0-degree edge
2 | 1D 90-degree edge
3 | 1D 135-degree edge
4 | 1D 45-degree edge
5 | Band
Notes: <number>

## Slide 3: Proposed Methods
<number>
SAO on/off flag for all color components for each LCU
Decouple SAO on/off from SAO type and signal ahead of merge flags
  SAO on/off flag for each color component
  SAO type
No merge occurs when SAO is off in left/upper LCU
  No signaling of merge left flag if SAO is off in the left LCU
  No signaling of merge up flag if SAO is off in the upper LCU
sao_type_idx | SAO type
0 | 1D 0-degree edge
1 | 1D 90-degree edge
2 | 1D 135-degree edge
3 | 1D 45-degree edge
4 | Band
Notes: <number>

## Slide 4: Proposed Methods
<number>
CABAC coding of SAO on/off flags
  1st bin (LCU) using 1st context model
  2nd bin (Y) using 2nd context model
  3rd bin and 4th bin (Cb/Cr) using 3rd context model
SAO merge flags can be removed for further simplification
  Both merge left and merge up can be removed
  Or, only merge up can be removed, which may require SAO parameter line buffer
SAO type can be efficiently coded as proposed in JCTVC-I0246
  SAO on/off
  EO/BO
  SAO sub-type (EO types or BO band position)
Notes: <number>

## Slide 5: Analysis of Number of Context Coded Bins
<number>
 | SAO LCU flag | merge left flag | merge up flag | SAO type | Total | Coding gain (%)
HM-7.0 | N/A | 13 = 3 | 13 = 3 | 63 = 18 | 24 | 0.0
JCTVC-I0193 | 8 | 13 = 3 | 13 = 3 | 53 = 15 | 29 | 
JCTVC-I0199 | 13 = 3 | 13 = 3 | 13 = 3 | 53 = 15 | 24 | 
JCTVC-I0601 | 1+13 = 4 | 13 = 3 | 13 = 3 | 53 = 15 | 25 | 0.3
I0601+no merge up | 1+13 = 4 | 13 = 3 | N/A | 53 = 15 | 22 | 0.2
I0601+no merge | 1+13 = 4 | N/A | N/A | 53 = 15 | 19 | 0.1
I0601+no merge+I0246 | 1+13 = 4 | N/A | N/A | 13 = 3 | 7 | 0.1
Notes: <number>

## Slide 6: Experimental Results
<number>
SAO LCU flag + merge removal + new SAO type
  0.6/0.2/0.1% for LCU size of 16/32/64 for Y (Main)
  LCU16
  LCU32
  LCU64
 | Main |  |  | HE10 |  | 
AI | -0.2% | -0.1% | -0.1% | -0.2% | -0.2% | -0.2%
RA | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2%
LDB | -1.1% | -0.7% | -1.0% | -1.0% | -0.9% | -0.7%
LDP | -1.0% | -0.8% | -0.7% | -0.9% | -0.8% | -0.8%
Ave | -0.6% | -0.4% | -0.5% | -0.6% | -0.5% | -0.5%
 | Main |  |  | HE10 |  | 
AI | 0.0% | 0.3% | 0.3% | 0.0% | 0.1% | 0.1%
RA | -0.2% | 0.4% | 0.1% | 0.1% | 0.1% | 0.1%
LDB | -0.4% | 0.2% | 0.4% | -0.3% | -0.3% | -0.2%
LDP | -0.3% | 0.8% | 0.8% | -0.2% | -0.1% | -0.1%
Ave | -0.2% | 0.4% | 0.4% | -0.1% | 0.0% | 0.0%
 | Main |  |  | HE10 |  | 
AI | 0.1% | 0.0% | 0.0% | 0.2% | 0.2% | 0.2%
RA | -0.2% | 0.1% | -0.1% | 0.0% | 0.2% | 0.0%
LDB | -0.2% | 0.4% | 0.7% | 0.0% | 0.3% | 0.4%
LDP | -0.1% | 0.9% | 1.0% | 0.1% | 0.5% | 0.5%
Ave | -0.1% | 0.4% | 0.4% | 0.1% | 0.3% | 0.3%
Notes: <number>

## Slide 7: Experimental Results
<number>
SAO LCU flag + merge removal
  0.6/0.2/0.1% for LCU size of 16/32/64 for Y (Main)
  LCU16
  LCU32
  LCU64
 |  |  |  | HE10 |  | 
AI | -0.2% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
RA | -0.3% | -0.1% | -0.1% | -0.2% | -0.2% | -0.3%
LDB | -1.0% | -0.6% | -0.9% | -1.0% | -0.9% | -0.7%
LDP | -1.0% | -0.6% | -0.7% | -0.9% | -0.6% | -0.9%
Ave | -0.6% | -0.4% | -0.5% | -0.6% | -0.5% | -0.5%
 |  |  |  | HE10 |  | 
AI | 0.0% | 0.3% | 0.4% | 0.0% | 0.1% | 0.1%
RA | -0.2% | 0.4% | 0.3% | 0.1% | 0.1% | 0.1%
LDB | -0.4% | 0.5% | 0.6% | -0.3% | -0.2% | -0.2%
LDP | -0.3% | 0.9% | 1.0% | -0.2% | 0.0% | -0.4%
Ave | -0.2% | 0.5% | 0.5% | -0.1% | 0.0% | -0.1%
 |  |  |  | HE10 |  | 
AI | 0.1% | 0.3% | 0.4% | 0.2% | 0.3% | 0.4%
RA | -0.2% | 0.3% | 0.2% | 0.1% | 0.3% | 0.3%
LDB | -0.2% | 0.8% | 1.0% | 0.0% | 0.3% | 0.6%
LDP | -0.1% | 1.2% | 1.6% | 0.1% | 0.8% | 0.6%
Ave | -0.1% | 0.6% | 0.8% | 0.1% | 0.4% | 0.5%
Notes: <number>

## Slide 8: Experimental Results
<number>
SAO LCU flag + merge up removal
  0.7/0.4/0.2% for LCU size of 16/32/64 for Y (Main)
  LCU16
  LCU32
  LCU64
 |  |  |  | HE10 |  | 
AI | -0.2% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
RA | -0.3% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2%
LDB | -1.0% | -0.9% | -0.8% | -1.0% | -1.0% | -0.8%
LDP | -1.2% | -0.9% | -0.7% | -0.9% | -0.8% | -0.8%
Ave | -0.7% | -0.5% | -0.4% | -0.6% | -0.5% | -0.5%
 |  |  |  | HE10 |  | 
AI | -0.1% | 0.2% | 0.2% | 0.0% | 0.0% | 0.0%
RA | -0.3% | 0.2% | 0.1% | -0.1% | -0.1% | 0.0%
LDB | -0.4% | 0.3% | 0.4% | -0.3% | -0.1% | 0.0%
LDP | -0.7% | 0.7% | 0.7% | -0.3% | -0.4% | -0.3%
Ave | -0.4% | 0.4% | 0.4% | -0.2% | -0.2% | -0.1%
 |  |  |  | HE10 |  | 
AI | 0.0% | 0.2% | 0.3% | 0.1% | 0.1% | 0.1%
RA | -0.3% | 0.2% | 0.1% | -0.1% | 0.0% | 0.0%
LDB | -0.3% | 0.6% | 0.6% | -0.2% | 0.2% | 0.5%
LDP | -0.3% | 0.8% | 1.1% | -0.2% | 0.4% | 0.3%
Ave | -0.2% | 0.5% | 0.5% | -0.1% | 0.2% | 0.3%
Notes: <number>

## Slide 9: Experimental Results
<number>
SAO LCU flag without merge removal
  0.7/0.5/0.3% for LCU size of 16/32/64 for Y (Main)
  LCU16
  LCU32
  LCU64
 |  |  |  | HE10 |  | 
AI | -0.2% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
RA | -0.3% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
LDB | -1.1% | -0.7% | -0.8% | -1.0% | -0.9% | -0.7%
LDP | -1.4% | -1.0% | -1.1% | -0.9% | -0.8% | -0.9%
Ave | -0.7% | -0.5% | -0.5% | -0.6% | -0.5% | -0.5%
 |  |  |  | HE10 |  | 
AI | -0.1% | 0.1% | 0.1% | -0.1% | 0.0% | 0.0%
RA | -0.3% | 0.1% | 0.0% | -0.2% | -0.2% | -0.1%
LDB | -0.6% | 0.3% | 0.2% | -0.4% | -0.3% | -0.3%
LDP | -1.0% | 0.3% | 0.4% | -0.5% | -0.3% | -0.3%
Ave | -0.5% | 0.2% | 0.2% | -0.3% | -0.2% | -0.2%
 |  |  |  | HE10 |  | 
AI | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0%
RA | -0.4% | 0.0% | 0.0% | -0.2% | 0.0% | 0.0%
LDB | -0.4% | 0.4% | 0.6% | -0.3% | 0.0% | 0.2%
LDP | -0.5% | 0.4% | 0.5% | -0.3% | 0.0% | -0.1%
Ave | -0.3% | 0.2% | 0.3% | -0.2% | 0.0% | 0.0%
Notes: <number>

## Slide 10: Conclusions
<number>
Proposed new SAO syntax to reduce complexity
SAO on/off is decoupled from SAO type
Number of context coded bins is reduced
Coding efficiency improvements by 0.6/0.2/0.1% for LCU size of 16/32/64 for Y (Main) with removal of merge flags
Coding efficiency improvements by 0.7/0.4/0.2% for LCU size of 16/32/64 for Y (Main) with removal of merge up flag
Recommend to adopt SAO LCU flag coding scheme
Notes: <number>