## Slide 1: coeff_abs_level_remaining maximum codeword length reduction (JCTVC-J0142)
Madhukar Budagavi and Vivienne Sze
Texas Instruments Inc.
Joint Collaborative Team on Video Coding (JCT-VC)
of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
10th Meeting: Stockholm, SE, 11–20 July 2012

## Slide 2: Introduction
HM-7.0 uses a combination of unary+VLC (golomb-rice+exp-golomb) for coding coeff_abs_level_remaining in bypass mode
  Prefix: Unary coded
  Suffix (for k = 0)
    Levels till 8 do not have suffix
    For other levels, suffix length increases as 1, 2, 3 …
  cParam varies in range 0,1, 2, 3, 4
  Maximum codeword length = 37 bits
Maximum codeword length <= 32 bits desirable
  Worst case throughput improvements
  Implementation complexity goes down as the number of coded bins go down
Further discussions assume cParam = 0

## Slide 3: HM-7.0 VLC for coeff_abs_level_remaining
Input Value | Codeword prefix | Codeword suffix | Prefix code length | Suffix code length | Total codeword length
0 | 0 |  | 1 | 0 | 1
1 | 10 |  | 2 | 0 | 2
2 | 110 |  | 3 | 0 | 3
3 | 1110 |  | 4 | 0 | 4
4 | 11110 |  | 5 | 0 | 5
5 | 111110 |  | 6 | 0 | 6
6 | 1111110 |  | 7 | 0 | 7
7 | 11111110 |  | 8 | 0 | 8
8 | 111111110 |  | 9 | 0 | 9
9~10 | 1111111110 | x | 10 | 1 | 11
11~14 | 11111111110 | xx | 11 | 2 | 13
15~22 | 111111111110 | xxx | 12 | 3 | 15
… | … | … | … | … | …
4103~8198 | 111111111111111111110 | xxxxxxxxxxxx | 21 | 12 | 33
8199~16390 | 1111111111111111111110 | xxxxxxxxxxxxx | 22 | 13 | 35
16391~32774 | 11111111111111111111110 | xxxxxxxxxxxxxx | 23 | 14 | 37

## Slide 4: Proposal 1: Maximum codeword length = 32
Input Value | Codeword prefix | Codeword suffix | Prefix code length | Suffix code length | Total codeword length
0 | 0 |  | 1 | 0 | 1
1 | 10 |  | 2 | 0 | 2
2 | 110 |  | 3 | 0 | 3
3 | 1110 |  | 4 | 0 | 4
4~5 | 11110 | x | 5 | 1 | 6
6~9 | 111110 | xx | 6 | 2 | 8
10~17 | 1111110 | xxx | 7 | 3 | 10
18~33 | 11111110 | xxxx | 8 | 4 | 12
… | … | … | … | … | …
2050~4097 | 111111111111110 | xxxxxxxxxxx | 15 | 11 | 26
4098~8193 | 1111111111111110 | xxxxxxxxxxxx | 16 | 12 | 28
8194~16385 | 11111111111111110 | xxxxxxxxxxxxx | 17 | 13 | 30
16386~32769 | 111111111111111110 | xxxxxxxxxxxxxx | 18 | 14 | 32

## Slide 5: Proposal 2: Prefix TU instead of Unary
Input Value | Codeword prefix | Codeword suffix | Prefix code length | Suffix code length | Total codeword length
0 | 0 |  | 1 | 0 | 1
1 | 10 |  | 2 | 0 | 2
2 | 110 |  | 3 | 0 | 3
3 | 1110 |  | 4 | 0 | 4
4 | 11110 |  | 5 | 0 | 5
5~6 | 111110 | x | 6 | 1 | 7
7~10 | 1111110 | xx | 7 | 2 | 9
11~18 | 11111110 | xxx | 8 | 3 | 11
… | … | … | … | … | …
2051~4098 | 1111111111111110 | xxxxxxxxxxx | 16 | 11 | 27
4099~8194 | 11111111111111110 | xxxxxxxxxxxx | 17 | 12 | 29
8195~16386 | 111111111111111110 | xxxxxxxxxxxxx | 18 | 13 | 31
16387~32770 | 111111111111111111 | xxxxxxxxxxxxxx | 18 | 14 | 32

## Slide 6: BD-Rate results (normal QP range)
 | Proposal 1 | Proposal 2
Maximum codeword length | 32 bits | 32 bits
AI-Main | 0.1% | 0.0%
RA-Main | 0.0% | 0.0%
LB-Main | 0.0% | 0.0%
LP-Main | 0.0% | 0.0%
AI-HE10 | 0.1% | 0.0%
RA-HE10 | 0.0% | 0.0%
LB-HE10 | 0.0% | 0.0%
LP-HE10 | 0.0% | 0.0%
Class F | 0.0% | 0.0%

## Slide 7: BD-Rate results (low QP range)
 | Proposal 1 | Proposal 2
Maximum codeword length | 32 bits | 32 bits
AI-Main | 0.1% | 0.0%
RA-Main | 0.1% | 0.0%
LB-Main | 0.1% | 0.0%
LP-Main | 0.1% | 0.0%
AI-HE10 | 0.1% | 0.0%
RA-HE10 | 0.1% | 0.0%
LB-HE10 | 0.1% | 0.0%
LP-HE10 | 0.1% | 0.0%
Class F | -0.8% | -0.6%

## Slide 8: Conclusions
Several VLCs with reduced maximum codeword length were studied
Average BD-Rate losses 0.0%
Class F BD-Rate savings in the range of: 0.4% - 0.6%
Other options tested
  TU-FLC135-L29: Smallest maximum codeword length of 29 bits

## Slide 9: Other variants

## Slide 10: Nomenclature
HM-7.0 will be denoted as U-FLC123-L37
  U denotes prefix is coded using unary
  FLC123 denotes suffix increases as 1-2-3
  L37 denotes maximum codeword length is 37 bits
Other variants of HM-7.0 VLC were studied with maximum codeword length between 29 to 32 bits
  Both unary prefix and truncated unary prefix variants studied
    Unary prefix allows for level range extension in future
    Truncated unary can be extended with a different cMax

## Slide 11: HM-7.0 VLC for coeff_abs_level_remaining
Input Value | Codeword prefix | Codeword suffix | Prefix code length | Suffix code length | Total codeword length
0 | 0 |  | 1 | 0 | 1
1 | 10 |  | 2 | 0 | 2
2 | 110 |  | 3 | 0 | 3
3 | 1110 |  | 4 | 0 | 4
4 | 11110 |  | 5 | 0 | 5
5 | 111110 |  | 6 | 0 | 6
6 | 1111110 |  | 7 | 0 | 7
7 | 11111110 |  | 8 | 0 | 8
8 | 111111110 |  | 9 | 0 | 9
9~10 | 1111111110 | x | 10 | 1 | 11
11~14 | 11111111110 | xx | 11 | 2 | 13
15~22 | 111111111110 | xxx | 12 | 3 | 15
… | … | … | … | … | …
4103~8198 | 111111111111111111110 | xxxxxxxxxxxx | 21 | 12 | 33
8199~16390 | 1111111111111111111110 | xxxxxxxxxxxxx | 22 | 13 | 35
16391~32774 | 11111111111111111111110 | xxxxxxxxxxxxxx | 23 | 14 | 37

## Slide 12: TU-FLC135-L29 proposal
Input Value | Codeword prefix | Codeword suffix | Prefix code length | Suffix code length | Total codeword length
0 | 0 |  | 1 | 0 | 1
1 | 10 |  | 2 | 0 | 2
2 | 110 |  | 3 | 0 | 3
3 | 1110 |  | 4 | 0 | 4
4 | 11110 |  | 5 | 0 | 5
5 | 111110 |  | 6 | 0 | 6
6~7 | 1111110 | x | 7 | 1 | 8
8~15 | 11111110 | xxx | 8 | 3 | 11
16~47 | 111111110 | xxxxx | 9 | 5 | 14
48~175 | 1111111110 | xxxxxxx | 10 | 7 | 17
176~687 | 11111111110 | xxxxxxxxx | 11 | 9 | 20
688~2735 | 111111111110 | xxxxxxxxxxx | 12 | 11 | 23
2736~10927 | 1111111111110 | xxxxxxxxxxxxx | 13 | 13 | 26
10928~43695 | 1111111111111 | xxxxxxxxxxxxxxx | 13 | 15 | 28

## Slide 13: BD-Rate results (normal QP range)
 | U-FLC135-L32 | U-FLC135-L30 | TU-FLC135-L29
Maximum codeword length | 32 bits | 30 bits | 29 bits
AI-Main | 0.0% | 0.0% | 0.0%
RA-Main | 0.0% | 0.0% | 0.0%
LB-Main | 0.0% | 0.0% | 0.0%
LP-Main | 0.0% | 0.0% | 0.0%
AI-HE10 | 0.0% | 0.0% | 0.0%
RA-HE10 | 0.0% | 0.0% | 0.0%
LB-HE10 | 0.0% | 0.0% | 0.0%
LP-HE10 | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0%

## Slide 14: BD-Rate results (low QP range)
 | U-FLC135-L32 | U-FLC135-L30 | TU-FLC135-L29
Maximum codeword length | 32 bits | 30 bits | 29 bits
AI-Main | 0.0% | 0.1% | 0.1%
RA-Main | 0.0% | 0.0% | 0.0%
LB-Main | 0.0% | 0.0% | 0.0%
LP-Main | 0.0% | 0.0% | 0.0%
AI-HE10 | 0.0% | 0.1% | 0.1%
RA-HE10 | 0.0% | 0.0% | 0.0%
LB-HE10 | 0.0% | 0.0% | 0.0%
LP-HE10 | 0.0% | 0.0% | 0.0%
Class F | -0.1% | -0.4% | -0.4%